## Slide 1: FreeSurfer Analyzing the Individual Subject
Bram Diamond
brdiamond@mgh.harvard.edu
FreeSurfer Help mailing list
freesurfer@nmr.mgh.harvard.edu
At-home FreeSurfer Course
https://surfer.nmr.mgh.harvard.edu/fswiki/TeachYourselfFreeSurfer
March 31st, 2020

## Slide 2: Talk Overview
Overview of the recon-all streamline
Specifics about the input image
Recon-all command breakdown
Introduction to subject directories and output files
(select) Streamline details
Brief overview of statistics
Where to find help

## Slide 3: Talk Overview
Overview of the recon-all streamline
Specifics about the input image
Recon-all command breakdown
Introduction to subject directories and output files
(select) Streamline details
Brief overview of statistics
Where to find help

## Slide 4: Overview of the Recon-all Streamline
T1 Weighted Input
Skull Stripping
Volumetric Labeling
Intensity Normalization
White Matter Segmentation
Surface Atlas Registration
Surface Extraction
Gyral Labeling

## Slide 5: Talk Overview
Overview of the recon-all streamline
Specifics about the input image
Recon-all command breakdown
Introduction to subject directories and output files
(select) Streamline details
Brief overview of statistics
Where to find help

## Slide 6: Input: T1 Weighted Image
T1 Contrast: white matter brighter than gray matter
~1mm3 (no more than 1.5mm)
Higher resolution may be worse!
Full Brain
Usually one acquisition is ok
MPRAGE (ME-MP-RAGE) or SPGR
1.5T or 3T
7T might have problems (hires flag)
Subject age > 5 years old
Brain has no major problems (i.e., tumors, parts missing)
Non-human primates possible
More MRI Pulse Sequence Parameter Details:
http://www.nmr.mgh.harvard.edu/~andre
http://adni.loni.usc.edu/methods/documents/mri-protocols

## Slide 7: Talk Overview
Overview of the recon-all streamline
Specifics about the input image
Recon-all command breakdown
Introduction to subject directories and output files
(select) Streamline details
Brief overview of statistics
Where to find help

## Slide 8: Fully Automated Reconstruction*
*“reconstruction” here refers to cortical reconstruction (surfaces), not k-space reconstruction.

## Slide 9: Fully Automated Reconstruction
file.dcm is a single DICOM file from the T1 MRI series
If you have more than one T1 image, then use two input (-i) flags:
  -i file1.dcm –i file2.dcm
You can use NIFTI as an input as well (mri_convert)
  -i file.nii

## Slide 10: Fully Automated Reconstruction
Finding file.dcm is sometimes difficult…
MR.1.3.12.2.1107.5.2.43.67026.201711091646082874533087
…
MR.1.3.12.2.1107.5.2.43.67026.2017110917193866363913436
MR.1.3.12.2.1107.5.2.43.67026.2017110916460831999633315 MR.1.3.12.2.1107.5.2.43.67026.2017110917194188432513634
MR.1.3.12.2.1107.5.2.43.67026.2017110916460832005833316 MR.1.3.12.2.1107.5.2.43.67026.2017110917194189797813639
MR.1.3.12.2.1107.5.2.43.67026.2017110916020777318078761
To get a list of acquisitions:
dcmunpack –src /path/to/dicoms
1 Localizer 3 40 15 1.171875 MR.1.3.12.2…
…
13 T1w_MPR_vNav_4eRMS … MR.1.3.12…
MP-RAGE T1 Protocol
This will be different for everyone
You will have to know what this name is

## Slide 11: Fully Automated Reconstruction
-i MR.1.3.12.2.1107.5.2.43.67026.2017110916020777318078761
A single DICOM file that belongs to the MPRAGE series (there might be several hundred; you only need one).
https://surfer.nmr.mgh.harvard.edu/fswiki/FsTutorial/Practice

## Slide 12: Fully Automated Reconstruction
“bert” is the “name” of the subject
recon-all creates a folder in $SUBJECTS_DIR named bert
All output goes in this folder (~400MB)
$SUBJECTS_DIR
bert
ernie
fsaverage
Notes: Always remember to set your $SUBJECTS_DIR variable:
csh  setenv SUBJECTS_DIR /path/to/subjects
sh  export SUBJECTS_DIR=/path/to/subjects

## Slide 13: Fully Automated Reconstruction
”all” means to do (almost) everything!
Can take 10-13 hours
recon-all –subject bert -autorecon-pial -autorecon3
recon-all –subject bert -autorecon2-wm -autorecon3
recon-all –subject bert -autorecon2-cp -autorecon3
You can run subsets of the processing stream to make it faster when correcting errors.
Many additional options
Notes: Always remember to set your $SUBJECTS_DIR variable:
csh  setenv SUBJECTS_DIR /path/to/subjects
sh  export SUBJECTS_DIR=/path/to/subjects

## Slide 14: Talk Overview
Overview of the recon-all streamline
Specifics about the input image
Recon-all command breakdown
Introduction to subject directories and output files
(select) Streamline details
Brief overview of statistics
Where to find help

## Slide 15: Fully Automated Reconstruction
Upon completion…
~400MB
recon-all.log
recon-all.done
recon-all.error
Just because it finishes “without error” does not mean that everything is ok!
Send us recon-all.log when you have problems! freesurfer@nmr.mgh.harvard.edu

## Slide 16: Fully Automated Reconstruction
Upon completion…
~400MB
orig.mgz
T1.mgz
brainmask.mgz
wm.mgz
aseg.mgz
rawavg.mgz
mgz = “compressed mgh” format (like nifti) unique to FreeSurfer
Native Anatomical Space
eg, 1x1x1.2mm3
256x256x128
“Conformed” Anatomical Space
1x1x1mm3 , 256x256x256

## Slide 17: Fully Automated Reconstruction
Upon completion…
lh.orig
lh.white
lh.pial
lh.inflated
lh.sphere.reg
rh.orig
rh.white
rh.pial
rh.inflated
rh.sphere.reg
Also…
lh.thickness and rh.thickness, ?h.curv, ?h.sulc

## Slide 18: Fully Automated Reconstruction
Upon completion…
lh.aparc.annot
lh.aparc.a2009s.annot
Desikan/Killiany Atlas
Destrieux Atlas

## Slide 19: Fully Automated Reconstruction
Upon completion…
aseg.stats – subcortical volumetric stats
wmparc.stats – white matter segmentation volumetric stats
lh.aparc.stats – left hemi Desikan/Killiany surface stats
rh.aparc.stats – right hemi Desikan/Killiany surface stats
lh.aparc.a2009.stats – left hemi Destrieux
rh.aparc.a2009.stats – right hemi Destrieux
lh.aparc.annot
Desikan/Killiany Atlas
lh.aparc.a2009s.annot
Destrieux Atlas

## Slide 20: Talk Overview
Overview of the recon-all streamline
Specifics about the input image
Recon-all command breakdown
Introduction to subject directories and output files
(select) Streamline details
Brief overview of statistics
Where to find help

## Slide 21: (select) Streamline details
T1 Weighted Input
Skull Stripping
Volumetric Labeling
Intensity Normalization
White Matter Segmentation
Surface Atlas Registration
Surface Extraction
Gyral Labeling

## Slide 22: Conform Step
Native Anatomical Space 1x1x1.1mm, 256x256x128, Sag
Conformed Anatomical Space 1x1x1mm, 256x256x256, Cor
“Anatomical Space”
orig.mgz
Surfaces
Parcellations
Segmentations
orig.mgz
rawavg.mgz
rawavg.mgz

## Slide 23: Talairach Transform
Computes 12 DOF transform matrix
Does NOT resample to Talaiarch space!
MNI305 template
Mostly used to report coordinates
transforms
talairach.xfm  text file with matrix

## Slide 24: Intensity Bias Correction
Outside of image is much brighter than inside (coils)
Worse with many coils
Makes gray/white segmentation difficult
Intensity Normalization (aka “Bias Correction”)
Raw Data
Corrected (T1.mgz)
T1.mgz

## Slide 25: Skull Strip
T1.mgz
brainmask.mgz (brain.mgz)
Removes all non-brain: Skull, eyes, neck and dura
brainmask.mgz

## Slide 26: Automatic Volume Labeling
Used to fill in subcortical structures for creating subcortical mass and ROI volume analysis
Named the “aseg.mgz”
Atlas: $FREESURFER_HOME/average/RB_all_2016-05-10.vc700.gca
aseg.mgz

## Slide 27: White Matter Segmentation
Separates white matter from everything else
Uses aseg volume to “fill in” subcortical structures
wm.mgz is not a very good name
  Cerebellum removed, brainstem still there
  Ventricles filled in
wm.mgz

## Slide 28: Fill and Cut (Subcortical Mass)
Fills in any holes
Removes any islands
Removes brain stem
Separates hemispheres (each hemi has different value)
filled.mgz = “subcortical mass”
wm volume (wm.mgz) filled volume (filled.mgz)

## Slide 29: Surface Extraction
Hemispheres separated
Fit to wm.mgz
1mm resolution
Rough, jagged surface
lh.orig
rh.orig
lh.orig
rh.orig

## Slide 30: Surface Model
Mesh (“finite element”)
Vertex = intersection at point of triangles
Vertex neighborhood
Each vertex has XYZ coordinates
Triangles/Faces ~ 300,000
Vertices ~ 140,000
Measures
  Area
  Distance
  Curvature
  Thickness

## Slide 31: White Matter Surface
orig surface
white surface
?h.white
Nudge orig surface
Follow T1 intensity gradients
Smoothness constraint
Vertex identity preserved

## Slide 32: Pial Surface
?h.pial
Nudge white surface
Follow T1 intensity gradients
Vertex identity preserved
Notes: Errors in pial surface placement are typically caused by underlying errors in the white matter placement
Errors can be corrected by interventions such as white matter control points.

## Slide 33: Volume vs. Surface Models
Volume
Uniform grid
Voxel is an intersection of grid lines
Columns, rows, slices
Voxel size/distance
Voxel assigned a value
XYZ
Surface
NON-uniform grid
Vertex is an intersection of triangles
Each vertex has an index
Distance between vertices ~1mm
Vertex assigned a value
XYZ

## Slide 34: Non-Cortical Areas of the Surface
?h.cortex.label
To check:
non-cortical regions are not errors!

## Slide 35: Inflation
White Surface
Pial Surface
Inflated Surface
2D surface in 3D space
Nudge vertices
No intensity gradient
See inside sulci
Used for sphere

## Slide 36: Cortical Thickness
Distance between white and pial surfaces
One value per vertex
Surface-based more accurate than volume-based
lh.thickness

## Slide 37: Curvature (Radial)
Circle tangent to surface at each vertex
Curvature measure is 1/radius of circle
One value per vertex
Signed (sulcus/gyrus)
lh.curv

## Slide 38: Spherical Registration
Sulcal Map
Spherical Inflation
Spherical Template
“fsaverage”
High-Dimensional
Non-linear
Registration

## Slide 39: Automatic Cortical Parcellation
Spherical Atlas based on manual labeling
Map to individual
through spherical registration
Fine-tune based on
individual anatomy
Note: Similar methodology to volume labeling

## Slide 40: Surface Overlays
lh.sulc on inflated
lh.curv on inflated
lh.thickness on inflated
lh.aparc.annot on inflated
lh.sulc on pial
fMRI on inflated
Value for each vertex
Color indicates value (grayscale, red/green, heat, color table)
Rendered on any surface
fMRI/stats maps too

## Slide 41: Talk Overview
Overview of the recon-all streamline
Specifics about the input image
Recon-all command breakdown
Introduction to subject directories and output files
(select) Streamline details
Brief overview of statistics
Where to find help

## Slide 42: ROI Summaries
Index SegId NVoxels Volume_mm3 StructName normMean normStdDev normMin normMax normRange
1 1 0 0.0 Left-Cerebral-Exterior 0.0000 0.0000 0.0000 0.0000 0.0000
2 2 265295 265295.0 Left-Cerebral-White-Matter 106.6763 8.3842 35.0000 169.0000 134.0000
3 3 251540 251540.0 Left-Cerebral-Cortex 81.8395 10.2448 29.0000 170.0000 141.0000
4 4 7347 7347.0 Left-Lateral-Ventricle 42.5800 12.7435 21.0000 90.0000 69.0000
5 5 431 431.0 Left-Inf-Lat-Vent 66.2805 11.4191 30.0000 95.0000 65.0000
6 6 0 0.0 Left-Cerebellum-Exterior 0.0000 0.0000 0.0000 0.0000 0.0000
….
Generating spreadsheets of group data
  asegstats2table --help
  aparcstats2table --help
aseg.stats – subcortical volumetric stats
wmparc.stats – white matter segmentation volumetric stats
lh.aparc.stats – left hemi Desikan/Killiany surface stats
rh.aparc.stats – right hemi Desikan/Killiany surface stats
lh.aparc.a2009.stats – left hemi Destrieux
rh.aparc.a2009.stats – right hemi Destrieux

## Slide 43: ROI Summaries
  During this course you will learn how to
    Using alternate atlases
    Hippocampal subfields, thalamic nuclei, brainstem
    Manipulating ROIs
    Making new *.stats files

## Slide 44: Quick Overview
recon-all.log
recon-all.done
recon-all.error
aseg.stats
?h.aparc.stats
…

## Slide 45: Talk Overview
Overview of the recon-all streamline
Specifics about the input image
Recon-all command breakdown
Introduction to subject directories and output files
(select) Streamline details
Brief overview of statistics
Where to find help

## Slide 46: Getting Your Questions Answered
recon-all –help
mri_convert -help
WIKI
Mail Archive
COMMAND HELP
SEND US YOUR QUESTIONS
freesurfer@nmr.mgh.harvard.edu
(Attach recon-all.log)
Notes: Continue with the Tutorials: Analyzing the Individual Subject Part and Part 2
The next live lecture is on Wednesday at 3:00PM ET on Intro to FreeView and working with data followed by ROI Analysis at 4:00PM ET.

## Slide 47: Thank You!
Bram Diamond
brdiamond@mgh.harvard.edu
FreeSurfer Help mailing list
freesurfer@nmr.mgh.harvard.edu
At-home FreeSurfer Course
https://surfer.nmr.mgh.harvard.edu/fswiki/TeachYourselfFreeSurfer

## Slide 48: Additional Slides

## Slide 49: Motion correction and averaging
001.mgz
002.mgz
rawavg.mgz
+
Does not change native resolution.
Usually only need one.
bert
orig
001.mgz 002.mgz
mri
rawavg.mgz

## Slide 50: The stages of recon-all
-autorecon1
-autorecon2
-autorecon3

## Slide 51: autorecon1
Volumetric Processing Stages (subjid/mri):
1. Motion Cor, Avg, Conform (orig.mgz)
2. Non-uniform inorm (nu.mgz)
3. Talairach transform computation (talairach/talairach.xfm)
4. Intensity Normalization 1 (T1.mgz)
5. Skull Strip (brainmask.mgz)
6. EM Register (linear volumetric registration)
7. CA Intensity Normalization (norm.mgz)
8. CA Non-linear Volumetric Registration
9. CA Label (Volumetric Labeling) (aseg.mgz)
10. Intensity Normalization 2 (T1.mgz)
11. White matter segmentation (wm.mgz)
12. Edit WM With ASeg
13. Fill and cut (filled.mgz)
Surface Processing Stages (subjid/surf):
14. Tessellate (?h.orig.nofix)
15. Smooth1
16. Inflate1
17. Sphere (?h.qsqhere)
18. Automatic Topology Fixer (?h.orig)
19. Final Surfs (?h.white ?h.pial ?.thickness)
20. Smooth2 (?h.smoothwm)
21. Inflate2 (?h.inflated)
22. Aseg Statistics (stats/aseg.stats)
23. Cortical Ribbon Mask (?h.ribbon.mgz)
24. Spherical Morph
25. Spherical Registration (?h.sphere.reg)
26. Map average curvature to subject
27. Cortical Parcellation (Labeling)
28. Cortical Parcellation Statistics
29. Cortical Parcellation mapped to Aseg
30. White Matter Parcellation (wmparc.mgz)
recon-all -help
Note: ?h.orig means lh.orig or rh.orig

## Slide 52: autorecon2
Volumetric Processing Stages (subjid/mri):
1. Motion Cor, Avg, Conform (orig.mgz)
2. Non-uniform inorm (nu.mgz)
3. Talairach transform computation (talairach/talairach.xfm)
4. Intensity Normalization 1 (T1.mgz)
5. Skull Strip (brainmask.mgz)
6. EM Register (linear volumetric registration)
7. CA Intensity Normalization (norm.mgz)
8. CA Non-linear Volumetric Registration
9. CA Label (Volumetric Labeling) (aseg.mgz)
10. Intensity Normalization 2 (T1.mgz)
11. White matter segmentation (wm.mgz)
12. Edit WM With ASeg
13. Fill and cut (filled.mgz)
Surface Processing Stages (subjid/surf):
14. Tessellate (?h.orig.nofix)
15. Smooth1
16. Inflate1
17. Sphere (?h.qsqhere)
18. Automatic Topology Fixer (?h.orig)
19. Final Surfs (?h.white ?h.pial ?.thickness)
20. Smooth2 (?h.smoothwm)
21. Inflate2 (?h.inflated)
22. Aseg Statistics (stats/aseg.stats)
23. Cortical Ribbon Mask (?h.ribbon.mgz)
24. Spherical Morph
25. Spherical Registration (?h.sphere.reg)
26. Map average curvature to subject
27. Cortical Parcellation (Labeling)
28. Cortical Parcellation Statistics
29. Cortical Parcellation mapped to Aseg
30. White Matter Parcellation (wmparc.mgz)
recon-all -help
Note: ?h.orig means lh.orig or rh.orig

## Slide 53: autorecon3
Volumetric Processing Stages (subjid/mri):
1. Motion Cor, Avg, Conform (orig.mgz)
2. Non-uniform inorm (nu.mgz)
3. Talairach transform computation (talairach/talairach.xfm)
4. Intensity Normalization 1 (T1.mgz)
5. Skull Strip (brainmask.mgz)
6. EM Register (linear volumetric registration)
7. CA Intensity Normalization (norm.mgz)
8. CA Non-linear Volumetric Registration
9. CA Label (Volumetric Labeling) (aseg.mgz)
10. Intensity Normalization 2 (T1.mgz)
11. White matter segmentation (wm.mgz)
12. Edit WM With ASeg
13. Fill and cut (filled.mgz)
Surface Processing Stages (subjid/surf):
14. Tessellate (?h.orig.nofix)
15. Smooth1
16. Inflate1
17. Sphere (?h.qsqhere)
18. Automatic Topology Fixer (?h.orig)
19. Final Surfs (?h.white ?h.pial ?.thickness)
20. Smooth2 (?h.smoothwm)
21. Inflate2 (?h.inflated)
22. Aseg Statistics (stats/aseg.stats)
23. Cortical Ribbon Mask (?h.ribbon.mgz)
24. Spherical Morph
25. Spherical Registration (?h.sphere.reg)
26. Map average curvature to subject
27. Cortical Parcellation (Labeling)
28. Cortical Parcellation Statistics
29. Cortical Parcellation mapped to Aseg
30. White Matter Parcellation (wmparc.mgz)
recon-all -help
Note: ?h.orig means lh.orig or rh.orig