## Slide 1
1
Anatomical Analysis with FreeSurfer surfer.nmr.mgh.harvard.edu
Notes: Look at reconstruction steps in depth
Serves to familiarize with reconstruction steps for individual subject.
Important to be familiar with steps for intervention, QA, troubleshooting errors you may encounter.
1

## Slide 2
2
Processing Stream Overview
Skull Stripping
Intensity Normalization
Volumetric Labeling
Surface Extraction
Surface Atlas
Registration
Gyral Labeling
White Matter
Segmentation
T1 Weighted
Input
Stats!
Notes: 2
-T1-weighted (wm brighter than gm)
-If higher res, gets downsampled (1mm isotropic)
-Can’t go lower than 1.5mm^3

## Slide 3
3
Input: T1 Weighted Image
T1 Contrast: white matter brighter than gray matter
~1mm3 (no more than 1.5mm)
Higher resolution may be worse!
Full Brain
Usually one acquisition is ok
MPRAGE or SPGR
1.5T or 3T
7T might have problems
Subject age > 5 years old
Brain has no major problems (ie, tumors, parts missing)
Non-human primates possible
More MRI Pulse Sequence Parameter Details:
http://www.nmr.mgh.harvard.edu/~andre
Notes: 3

## Slide 4
4
Fully Automated Reconstruction*
recon-all –i file.dcm –subject bert –all
* “Reconstruction” here refers to cortical reconstruction, not k-space reconstruction.
Notes: Command to get start reconstruction
Recon-all
Single dicom from T1 dicom series
4

## Slide 5
5
Fully Automated Reconstruction
recon-all
–i file.dcm
–subject bert
–all
file.dcm is a single DICOM file from the T1 MRI series.
If you have more than one T1, then use:
–i file1.dcm –i file2.dcm
You can use NIFTI as well with
–i file.nii
To get a list of acquisitions:
dcmunpack –src /path/to/dicoms
Notes: Command to get start reconstruction
Recon-all
Single dicom from T1 dicom series
5

## Slide 6
6
Fully Automated Reconstruction
recon-all
–i file.dcm
–subject bert
–all
“bert” is the “name” of the subject
Creates a folder in $SUBJECTS_DIR
All output goes in this folder (~400MB)
Other subjects in $SUBJECTS_DIR
bert
$SUBJECTS_DIR
ernie
fsaverage …
setenv SUBJECTS_DIR /path/to/space
Notes: Command to get start reconstruction
Recon-all
Single dicom from T1 dicom series
6

## Slide 7
7
Fully Automated Reconstruction
recon-all
–i file.dcm
–subject bert
–all
-all means to do everything!
Can take 10-20 hours
Later, we will show you how to run subsets of the processing stream to make it faster when correcting errors.
Notes: Command to get start reconstruction
Recon-all
Single dicom from T1 dicom series
7

## Slide 8
8
Upon Completion…
$SUBJECTS_DIR/bert
scripts mri surf label stats
recon-all –i file.dcm –subject bert –all
~400MB
Notes: 8
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 9
9
Upon Completion…
bert
scripts mri surf label stats
recon-all.log
recon-all.done
Just because it finishes “without error” does not mean that everything is ok!
Send us recon-all.log when you have problems! freesurfer@nmr.mgh.harvard.edu
Notes: 9
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 10
10
Upon Completion…
bert
scripts mri surf label stats
orig.mgz
T1.mgz
brainmask.mgz
wm.mgz
aseg.mgz
mgz = “compressed mgh” format (like nifti) unique to FreeSurfer
rawavg.mgz
others: nu.mgz, norm.mgz, wmparc.mgz, aparc+aseg.mgz, ribbon.mgz
Notes: 10
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 11
11
Upon Completion…
bert
scripts mri surf label stats
orig.mgz
T1.mgz
brainmask.mgz
wm.mgz
aseg.mgz
rawavg.mgz
Native Anatomical Space
eg, 1x1x1.2mm3 , 256x256x128
“Conformed” Anatomical Space
1x1x1mm3 , 256x256x256
Notes: 11
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 12
Native Anatomical Space 1x1x1.1mm, 256x256x128, Sag
Conformed Anatomical Space 1x1x1mm, 256x256x256, Cor
“Anatomical Space”
orig.mgz
Surfaces
Parcellations
Segmentations
Conform Step
orig.mgz
mri
rawavg.mgz
bert
rawavg.mgz

## Slide 13
13
Upon Completion…
bert
scripts mri surf label stats
lh.orig
lh.white
lh.pial
lh.inflated
lh.sphere.reg
rh.orig
rh.white
rh.pial
rh.inflated
rh.sphere.reg
lh.thickness and rh.thickness, ?h.curv, ?h.sulc
Notes: 13
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 14
14
Upon Completion…
bert
scripts mri surf label stats
lh.aparc.annot
rh.aparc.annot
lh.aparc.a2009s.annot
rh.aparc.a2009s.annot
Desikan/Killiany Atlas
Destrieux Atlas
Notes: 14
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 15
15
Upon Completion…
bert
scripts mri surf label stats
aseg.stats – subcortical volumetric stats
wmparc.stats – white matter segmentation volumetric stats
lh.aparc.stats – left hemi Desikan/Killiany surface stats
rh.aparc.stats – right hemi Desikan/Killiany surface stats
lh.aparc.a2009.stats – left hemi Destrieux
rh.aparc.a2009.stats – right hemi Destrieux
stats files are text files with summary information, eg:
volume of left amygdala
average thickness in superior temporal gyrus
Notes: 15
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 16
Some of the Processing Steps…
16
Notes: 16

## Slide 17
17
Motion Correction and Averaging
001.mgz
002.mgz
+
rawavg.mgz
orig
001.mgz 002.mgz
mri
rawavg.mgz
Does not change native resolution.
Usually only need one.
bert
Notes: FS dir structure illustrated on slides
Can give more than one, then avg to rawavg.
used to be that 2 acqs recommended, now with 3T, 32ch, MEMPRAGE, one recommended. still beneficial to collect to acquisitions, then use one with best contrast, one or 2, make sure it's consistent.
2 mprage at 1.5
1 mprage at 3t (SNR is good) - only use 1 or 2 for all subjects
-uses robust_register, no longer fsl
17

## Slide 18
18
Talairach Transform
Computes 12 DOF transform matrix
Does NOT resample to Talaiarch space!
MNI305 template
Mostly used to report coordinates
transforms
talairach.xfm  text file with matrix
bert
scripts mri surf label stats
Notes: computes transformation matrix, using MNI305 template, not resampling – just transform
Tells FS how to get from anatomical space -> MNI space (contains talairach labels)
Montreal Neurological Institute
18

## Slide 19
19
Intensity Bias
Left side of the image much brighter than right side
Worse with many coils
Makes gray/white segmentation difficult
mri
T1.mgz
bert
Notes: -Remove bias from the coil. brain areas closer to coil are brighter than others, get rid of bias.
-Hard to see with human eye, demonstrates map of intensity bias. Want to make it uniform.
-No coils in middle of brain (poorer SNR, CNR).
19

## Slide 20
20
Skull Strip
Removes all non-brain
  Skull, Eyes, Neck, Dura
brainmask.mgz (cf, brain.mgz)
T1.mgz
brainmask.mgz
brainmask.mgz
mri
bert
Notes: remove non brain areas, gives us brainmask (work with it a lot). Again, helps with wm/gm seg

## Slide 21
21
Automatic Volume Labeling
Used to fill in subcortical structures for creating subcortical mass
Useful in its own right
aseg.mgz
More in ROI Talk
ASeg Volume
aseg.mgz
mri
bert
Atlas: $FREESURFER_HOME/average/RB_all_2008-03-26
Notes: -Automatic segmentation (multi source of info), known intensity profiles, neighborhood relations, probability of voxel label given spatial location
-get stats for subcortical structures
Several papers on FS wiki detailing sub-cortical segmentation in FS
See ROI talk online, plus tutorial
21

## Slide 22
22
“White Matter” Segmentation
Separates white matter from everything else
Uses aseg to “fill in” subcortical structures
Cerebellum removed, brain stem still there
wm.mgz -- “wm” not a very good name!
wm.mgz
mri
bert
Notes: 22

## Slide 23
23
Fill and Cut (Subcortical Mass)
WM Volume (wm.mgz)
Filled Volume (filled.mgz)
(Subcortical Mass)
Fills in any holes.
Removes any islands
Removes brain stem
Separates hemispheres (each hemi has different value)
filled.mgz = “Subcortical Mass”
Notes: Final step: prepare for generating wm surf
Separate mask, one side per hemi, each hemi gets separate surface.
23

## Slide 24
24
Surface Extraction
Hemispheres separated
Fit to wm.mgz
1mm resolution
Rough, jagged
wm.mgz
lh.orig
rh.orig
surf
bert
lh.orig
rh.orig
Notes: 24
-label all wm, fills in ventricles and other structures based on aseg. Mask to extract wm.
Ventricles are filled in (as are the other subcortical structures).
Set of histograms in axial/horizontal plane, highest peak in each histo near center of image classified as wm (most voxels), checks across slices to make sure classification consistent, centers wm intensities on 110.

## Slide 25
25
Surface Model
Mesh (“Finite Element”)
Vertex = point of triangles
Neighborhood
XYZ at each vertex
Triangles/Faces ~ 300,000
Vertices ~ 140,000
Area, Distance
Curvature, Thickness
Notes: 25
-mesh allows FS to get various measurements
-all triangles meet at various points called vertices – measurements stored there (area = area of all triangles)
-XYZ - each vertex has a label (important for cross-subject reg)
Once the xyz of each corner of each triangle is known, then it is possible to characterize the entire cortical surface in terms of area, distance, curvature, and thickness.
The cortical surface is represented by a finite element model using triangles to cover the cortical surface. The reconstruction is the (mostly automated) process of assigning an xyz to each corner of each triangle.

## Slide 26
26
Volume vs Surface Model
Volume
uniform grid
voxel is an intersection of grid lines
columns, rows, slices
voxel size/distance
voxel assigned a value
XYZ
Surface
NON-uniform grid
vertex is an intersection of triangles
each vertex has an index
distance between vertices ~1mm
vertex assigned a value
XYZ
Vector of vertex values (~140,000)
Notes: 26

## Slide 27
27
White Matter Surface
Nudge orig surface
Follow T1 intensity gradients
Smoothness constraint
Vertex identity preserved
orig surface
white surface
lh.white
rh.white
Notes: 27

## Slide 28
28
Pial Surface
Nudge white surface
Follow T1 intensity gradients
Vertex identity preserved
Notes: Use finalized wm as starting point, pial grow out from wm surf, find fall off of gm and CSF,
28

## Slide 29: Pial surf grows from white surf
Errors in pial surface placement are typically caused by underlying errors in the white matter placement, and can be corrected by interventions such as white matter control points.

## Slide 30
30
Non-Cortical Areas of Surface
Amygdala, Putamen, Hippocampus, Caudate, Ventricles, CC
?h.cortex.label
Notes: certain part of medial wall not included in any cortical measures. Filled in to create continuous surface, makes certain calculations easier
image of masked out area,
view in three different planes.
30

## Slide 31: Inflation: 2D Surface in 3D Space
31
White Surface
Pial Surface
Nudge vertices
No intensity constraint
See inside sulci
Used for sphere
Notes: 31

## Slide 32
32
Cortical Thickness
white/gray surface
pial surface
lh.thickness, rh.thickness
Distance between white and pial surfaces
One value per vertex
Surface-based more accurate than volume-based
mm
Notes: -Now that you have wm & pial surfs…get cort meas
-calculates cort thick, distance between vertices on wm and gm. blue dots are vertices (indicated by). dist from wm to gm, and gm to wm and takes average.
32

## Slide 33
33
Curvature (Radial)
Circle tangent to surface at each vertex
Curvature measure is 1/radius of circle
One value per vertex
Signed (sulcus/gyrus)
lh.curv, rh.curv
Notes: -there is a curvature for pial surface and curvature for white surface at every vertex
Curvature = ratio , 1/radius of circle best matches what’s going on at each vertex in all directions
-indicates how curvy at each vertex (not sulcul depth).
How bumpy, nothing to do with sulci/gyri
33

## Slide 34
34
Spherical Registration
Sulcal Map
Spherical Inflation
High-Dimensional
Non-linear
Registration to
Spherical Template
Atlas template is called “fsaverage”
More in surface-based analysis talk.
Notes: 34
main reason to use FS, this stage (important slide).
Now we have surfs that can be inflated, (a) inflate to sphere, (b) align to template, (c) then put subject back into original space.
Template = fsaverage (40 adults ranging in age), we do not recommend processing MRI datasets with subjects younger than 4/5 years of age. Atlas built using adult data, prior information related to intensities and structures not representative of younger populations. Pediatric atlas is in the works (Lilla).

## Slide 35
35
Automatic Cortical Parcellation
Fine-tune based on
individual anatomy
Spherical Atlas based on Manual Labeling
Map to Individual
Thru Spherical Reg
Note: Similar methodology to volume labeling
More in the Anatomical ROI talk
Notes: -subject aligned to spherical atlas, take labels from cortparc atlas and apply to individ subject, since anatomical boundaries are matched up.
not just throwing labels on there, using individual anatomy to fine tune labels.
35

## Slide 36
36
Surface Overlays
lh.sulc on inflated
lh.curv on inflated
lh.thickness on inflated
Value for each vertex
Color indicates value
Color: gray, red/green, heat, color table
Rendered on any surface
fMRI/Stat Maps too
lh.aparc.annot on inflated
lh.sulc on pial
lh.curv on inflated
fMRI on inflated
Notes: 36
Name some of them.
All surfaces have the same number of vertices. Different surfaces are made by moving the triangles around to achieve some goal. There is a one-to-one correspondence between surfaces which allows the user to cross-reference vertices from one surface to another (even across subjects) and to the volume. This feature is critical to get properly oriented. In the flat surface, there’s still a one-to-one correspondence, but not all vertices in the orig surface may be represented.

## Slide 37
37
ROI Summaries:
Index SegId NVoxels Volume_mm3 StructName normMean normStdDev normMin normMax normRange
1 1 0 0.0 Left-Cerebral-Exterior 0.0000 0.0000 0.0000 0.0000 0.0000
2 2 265295 265295.0 Left-Cerebral-White-Matter 106.6763 8.3842 35.0000 169.0000 134.0000
3 3 251540 251540.0 Left-Cerebral-Cortex 81.8395 10.2448 29.0000 170.0000 141.0000
4 4 7347 7347.0 Left-Lateral-Ventricle 42.5800 12.7435 21.0000 90.0000 69.0000
5 5 431 431.0 Left-Inf-Lat-Vent 66.2805 11.4191 30.0000 95.0000 65.0000
6 6 0 0.0 Left-Cerebellum-Exterior 0.0000 0.0000 0.0000 0.0000 0.0000
….
$SUBJECTS_DIR/bert/stats
aseg.stats – volume summaries
?h.aparc.stats – desikan/killiany surface summaries
?h.aparc.a2009s.stats – destrieux surface summaries
wmparc.stats – white matter parcellation
Routines to generate spread sheets of group data
asegstats2table --help
aparcstats2table --help
More info in Anatomical ROI talk.
Notes: Stats, subcortical from aseg, cortical from surfaces
Found in scripts dir
Have functions to compile individual subjects stats, select certain ROIs, or all.
37

## Slide 38
38
Upon Completion of recon-all
$SUBJECTS_DIR /bert
scripts mri surf label stats
recon-all –i file.dcm –subject bert –all
orig.mgz
lh.inflated
lh.aparc.annot
aseg.stats
recon-all.log
Notes: 38
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 39
39
Getting FreeSurfer
surfer.nmr.mgh.harvard.edu
  Register
  Download
  Mailing List
Wiki: surfer.nmr.mgh.harvard.edu/fswiki
Platforms:
  Linux
  Mac
  Windows (VirtualBox)
Installed in $FREESURFER_HOME

## Slide 40: Download & Install

## Slide 41: What to do next
Notes: Directions on where to get tutorial data & how to run recon-all on QuickInstall wiki

## Slide 42: Getting Answers
Mail Archive
42
Wiki
recon-all -help
mri_convert -help
$FREESURFER_HOME/docs
Send questions to:
freesurfer@nmr.mgh.harvard.edu
Notes: 42

## Slide 43
43
Overview
recon-all –i file.dcm –subject bert –all
Notes: Recon-all command
GUI – graphical user interface
Familiar with…
43

## Slide 44
44
Tutorial Tips
Best not to run multiple instances of Freeview at the same time unless you have > 8GB RAM.
If you are running a command in the foreground, you should not type additional commands in that terminal (command prompt will be missing)
Right
Left
Volume Viewer (Freeview) Radiological Orientation
Notes: 44

## Slide 45
45
What is the "subject"?
What is the SUBJECTS_DIR?
What does it mean to conform the volume?
Are the FS results in Talairach/mni305 or native space?
What is the wm.mgz file?
What is the medial wall?
Will the surface be accurate in the medial wall?
What is the difference between a surface and a surface overlay?
What does "?h" mean?
How do you get help?
Pop Quiz!
Notes: 45

## Slide 46
46
End of Presentation
http://www.bostonglobe.com/ideas/2017/09/15/uncommon-knowledge-from-rent-rivalry/UzTx3m7HSyweIlav2EB6QL/story.html
Notes: 46

## Slide 47
47
Intensity Normalization
Removes B1 bias field
NU (MNI) nu.mgz
Presegmentation (T1.mgz)
  Most WM = 110 intensity
  Pre- and Post-Skull Strip
nu.mgz
mri
bert
T1.mgz
T1.mgz
nu.mgz
110.9 ±1.8
108.9 ±1.5
110.0 ±0.0
Notes: Nu volume created – bias removed
T1 – adjust intensity so that wm is around 110
Makes wm segment easier and generate wm surface
The B1 bias field is estimated by measuring the variation in the white matter intensity. The main body of the white matter is used to estimate the field across the entire volume. The intensity at each voxel is then divided by the estimated bias field at that location in order to remove the effect of the bias field.
Intensity = brightness of voxel – ideally only indicative of the MR params of the tissue (PD, T2, T1).
GM = dark, WM = bright.
Bias = changes in intensity across space that are unrelated to biology. i.e. tissue gets further away from receive coil, gets darker in intensity. When talking about bias, referring to biologically unrelated fluctuations in intensity.

## Slide 48
48
Results
Volumes
Surfaces
Surface Overlays
ROI Summaries
Notes: All organize in each subjects folder in SUBJECTS_DIR path
48

## Slide 49
49
Volumes
orig.mgz
$SUBJECTS_DIR/bert/mri
All “Conformed” 2563, 1mm3
Many more …
aseg.mgz
T1.mgz
brainmask.mgz
wm.mgz
filled.mgz
Subcortical Mass
aparc+aseg.mgz
Volume Viewer:
tkmedit
Notes: 49
Overview of main volumes created. most important ones brainmask, wm.mgz (editing, fix topos).
use tkmedit to view/edit

## Slide 50
50
Surfaces
orig
white
pial
inflated
sphere,sphere.reg
patch (flattened)
$SUBJECTS_DIR/bert/surf
Number/Identity of vertices stays the same (except patches)
XYZ Location Changes
Flattening not done as part of standard reconstruction
Surface Viewer:
tksurfer
Notes: 50
-All surfaces have the same number of vertices (within one subject??)
-There is a one-to-one correspondence between surfaces which allows the user to cross-reference vertices from one surface to another (even across subjects) and to the volume.
Different surfaces are made by moving the triangles around to achieve some goal. This feature is critical to get properly oriented. In the flat surface, there’s still a one-to-one correspondence, but not all vertices in the orig surface may be represented.

## Slide 51
51
Topological Defects
Fornix
Pallidum and Putamen
hippocampus
Ventricles and Caudate
Cortical Defects
Holes
Handles
Automatically Fixed
Notes: Examples of topo defects on surface which should be corrected.
-cut handles
-fill holes
51

## Slide 52
52
Subject Folder Directory Tree
bert
scripts mri surf label stats
orig.mgz T1.mgz brain.mgz wm.mgz aseg.mgz
recon-all –i file.dcm –subject bert –all
Notes: 52
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 53
53
Surface Reconstruction Overview
Input: T1-weighted (MPRAGE,SPGR)
Find white/gray surface
Find pial surface
“Find” = create mesh
  Vertices, neighbors, triangles, coordinates
  Accurately follows boundaries between tissue types
  “Topologically Correct”
    closed surface, no donut holes
    no self-intersections
Generate surface-based cross-subject registration
Label cortical folding patterns
Subcortical Segmentation along the way
Notes: 53

## Slide 54
54
Find “Subcortical Mass”
All White Matter
All Subcortical Structures
Ventricles
Excludes brain stem and cerebellum
Hemispheres separated
Connected (no islands)
Many Stages … More Later …
Notes: Overall goal, extract wm along with subcortical structures
After certain point hemis processed seperately
54

## Slide 55
55
MGZ File Format
001.mgz
mgz = compressed MGH file
Can store 4D (like NIFTI)
cols, rows, slices, frames
Generic: volumes and Surfaces
Eg, Typical Anatomical volume: 256 x 256 x 128 x 1
“Volume-encoded” Surface Files
nvertices, 1, 1, frames (eg, 163214 x 1 x 1 x 40)
No geometry information
lh.thickness.sm10.mgz
Notes: FS uses special file format (volumes FS creates in this format)
-do not need to convert dicom or nifti, FS does this (using mri_convert)
-A frame is the 4th dimension which is the variable you are analyzing. The first 3 dimensions are spatial and the fourth is the variable (schizophrenics vs. controls).
-analyze format is SPM format; “Siemens IMA” and AFNI is fmri software
55

## Slide 56
56
Other File Formats
Surface: Vertices, XYZ, neighbors (lh.white)
Curv: lh.curv, lh.sulc, lh.thickness
Annotation: lh.aparc.annot
Label: lh.pericalcarine.label
Unique to FreeSurfer
FreeSurfer can read/write:
  NIFTI, Analyze, MINC
FreeSurfer can read:
  DICOM, Siemens IMA, AFNI
Notes: Curv: surface overlay (stats visualized on surface)
Annot: surface label
Label: volumetric label
FS read and write variety of formats
56

## Slide 57
57
Fully Automated Reconstruction
Come back in 20 hours …
Check your results – do the white and pial surfaces follow the boundaries?
-- Can be broken up
Launch reconstruction:
recon-all –i file.dcm –subject bert –all
Where file.dcm is one file from the correct (T1-weighted)
MR series.
Notes: -all: perform all standard recon steps
-not so distant future, sig less time
-visually inspect results
Certain functions implemented using CUDA to take advantage of GPU
Collaboration with IBM to implement OpenMP versions of certain functions
57

## Slide 58
58
SUBJECTS_DIR Environment Variable
bert
$SUBJECTS_DIR
fred
jenny
margaret …
Subject
recon-all –i file.dcm –subject bert –all
Notes: 58
-Necessary to tell FS where your data, where to save output.
-Each unique subject has standard sub-directory heirarchy, organizes the output (volumes, surfs, logs, stats, etc.)

## Slide 59
59
FreeSurfer Directory Tree
bert
scripts surf label mri stats
orig.mgz T1.mgz brain.mgz wm.mgz aseg.mgz
Subject
Subject Name
Each data set has its own unique SubjectId (eg, bert)
recon-all –i file.dcm –subject bert –all
Notes: 59
-bert is ID, dirs underneath bert created automatically.
-Most important ones: stats, mri, scripts(logs)
-a lot of files stored here are in a format called…

## Slide 60
60
Sulcal Depth
lh.sulc, rh.sulc
lh.curv, rh.curv
Notes: Distance vertex travel from wm/pial surface to ?h.inflated version.
Less detail than curv measure
?h.sulc (sulcal depth) used to register (grossly align) with atlas
?h.curv to tweak alignment to take individual anatomy into account.
Another cortical measure
Show to prove curv not sulcal depth
60

## Slide 61
61
Tessellation and Topology Fixing
Mosaic of triangles (“tessellation”)
Errors: Donut holes, handles
Automatic topology fixer
orig surface
surf/lh.orig
surf/rh.orig
Notes: lay mesh of triangles around wm.mgz,
-original guess(first draft) at wm surface, contains some errors (subsequently fixed)
-dont think as one slice, but over entire brain.
61

## Slide 62: Pial surf grows from white surf