## Slide 1
Longitudinal FreeSurfer
Martin Reuter
HMS/MGH/MIT Athinoula A. Martinos Center
for Biomedical Imaging

## Slide 2
What can we do?
measure volume of cortical or subcortical structures
compute thickness (locally) of the cortical sheet
study differences of populations (diseased, control)‏
We'd like to:
exploit longitudinal information
(same subject, different time points)‏

## Slide 3
Why longitudinal?
to reduce intra-individual morphological variability
to detect small changes
to follow disease progression (atrophy)‏
to better estimate time to onset
(e.g. Huntington's disease)‏
to study effects of drug treatment
...

## Slide 4
How can it be done?
Avoid the problem of massive inter-subject anatomical variability
Use each subject as their own control
Stay unbiased w.r.t. any specific time point
Longitudinal Design:
  Create a template (base) as an initial guess for segmentation and reconstruction
  Initialize each time point with the base to reduce variability in the optimization process
  For this we need a robust registration (rigid)
  and template estimation

## Slide 5
Robust Registration
Using robust statistics:
    M-estimators:
    Tukey-Biweight to reduce influence of outliers
    Solved with iterative re-weighted least squares
Symmetric alignment in 'half way space'
Hierarchical (Gaussian Pyramid)‏
With initialization (moments)‏
Highly accurate registrations,
even with noise or outliers (B0 distortions,
gradient non-linearities, jaw movement, ...)‏

## Slide 6
Robust Registration (c.f. Nestares and Heeger, 2000)‏
Square
Tukey's Biweight
The contribution of error is limited for outliers:

## Slide 7
Robust Registration
Left: aligned image with weights (red outlier)‏
Right: differences of source and target

## Slide 8
Robust Registration
Target
Target

## Slide 9
Robust Registration
Registered Src FSL FLIRT
Registered Src Robust

## Slide 10
Accuracy of mri_robust_register

## Slide 11
Robust Template
For N images we would like to have:
  a common space (to be able to compare across time)‏
  a template image (mean/median) of all images
Common space:
  for 2 this is the halfway space (sqrt of transform)‏
  for more image we need an iterative construction
Template (Fréchet Mean):
  in each iteration we create a mean or median image
  then register all images with this template
  until convergence is reached
  for better performance: compute an approx. of the final location and use as initialization

## Slide 12
Robust Template
Aligned Images
Template Image

## Slide 13
Advantages of Robust Template
Unbiased
Common space for computing:
    TIV (ICV) estimation (as changes over time are blurred out) and TIV should stay constant
    Skull stripping across time
    Talairach transform
    Basis for non-uniformity correction
    Common component of the nonlinear registration
Command: mri_robust_template

## Slide 14
Initializing Longitudinal Processing
Treat all time points equivalently to avoid bias.
Would like to include some information that much of the anatomy is the same over time, but don’t want to lose sensitivity to disease effects.
Incorporate a Parzen window to use image intensity across time as a similarity measure (this amounts to probabilistic voting).
Window size of Parzen can be estimated directly from robust cross-time noise.

## Slide 15
FreeSurfer Commands (recon-all)‏
1. Run everything cross sectionally (independently)‏
2. The -base flag creates the robust template
and runs it through FreeSurfer:
recon-all -base baseid -tp tp1id \ -tp tp2id ... -all
3. Use base to initialize the -longitudinal runs:
recon-all -long tpNid baseid -all
This creates the directories tpNid.long.baseid
4. The stats of these runs can now be compared

## Slide 16
Test-Retest

## Slide 17
Test-Retest (Bias)‏

## Slide 18
Simulated Atrophy
Cross sectional RED, longitudinal GREEN
Simulated atrophy was applied to the left hippocampus only
Left Hippocampus
Right Hippocampus

## Slide 19
Still to come ...
More Tests (especially with real atrophy)‏
Improvements:
    Common warps (non-linear)
    Intracranial Volume Estimation
    Intensity Normalization
    Initial Surface Placement
    Spherical Registration
http://surfer.nmr.mgh.harvard.edu/fswiki/LongitudinalProcessing
Thanks to: the FreeSurfer Team,
specifically Bruce Fischl and Nick Schmansky