## Slide 1: Integrating FreeSurfer and FSL FEAT

## Slide 2
Outline
Registering FEAT  FreeSurfer Anatomical
  Automatic (FLIRT)
  Manual (tkregister2)
Viewing FEAT output on Anatomical
Sampling FEAT output on the surface
  Individual
  Common Surface Space (Atlas/fsaverage)
Mapping FreeSurfer Segmentations to FEAT
Group Analysis

## Slide 3: Registration
FreeSurfer Anatomical (orig)
Template Functional
Note: Registering the template functional volume to the anatomical volume is sufficient
to register the template to the surface.

## Slide 4
FreeSurfer Registration
FreeSurfer
Subject-Specific
  Volumes
  Surfaces
  Thickness
  ROIs
Your Data/Software
  fMRI (FSL, etc)
  EEG/MEG
  DTI
  …
Registration
Registration Matrix
Affine 4x4
As many as 12 DOF (usually 6)
Text file

## Slide 5: Automatic Registration
reg-feat2anat –featdir fbert1.feat –subject bert
Uses FLIRT to perform 6DOF registration:
fbert1.feat/example_func.nii.gz
$SUBJECTS_DIR/bert/mri/brainmask.mgz
Creates FreeSurfer registration matrix:
fbert1.feat/reg/freesurfer/anat2exf.register.dat
reg-feat2anat --help
First: analyze your data with FEAT (No Smoothing)
Also creates: fbert1.feat/reg/freesurfer/anat2std.register.dat
This matrix maps standard space to anatomical space and can be used when combining data within subject across data sets

## Slide 6: Manual Registration
tkregister2 --help
reg-feat2anat –feat fbert.feat --manual
Visually inspect registration
Manually edit registration (6 DOF)
Cf Manual Talairach registration

## Slide 7: Tips
Rigid = 6 DOF = No stretching
Use CSF to get a sense of where the folds are
Avoid using B0 distortion regions
Avoid using ventricles
Warning about “edge” of the brain
Same Subject, Left-Right Flips

## Slide 8: Viewing Functional Activation on the Volume
tkmedit bert orig.mgz -aux brain.mgz
-overlay ./fbert1.feat/stats/zstat1.nii.gz
-overlay-reg ./fbert1.feat/reg/freesurfer/anat2exf.register.dat
-fthresh 2.3 –fmax 4.3 -seg aparc+aseg.mgz
Thresholds depend on the nature of the data,
Eg, for zstat image, 2.3 means z > 2.3
Can be changed with
View->Configure->FunctionalOverlay
Visual, Auditory, Motor
Can display any functional data, eg,
zstat, fzstat, cope, pe, etc

## Slide 9
Sampling on the Surface
White/Gray
Pial
White/Gray
Pial
Half Way
Average
Projection Fraction
--projfrac 0.5

## Slide 10
Sampling on the Surface

## Slide 11: Viewing FEAT Stats on the Surface
tksurfer bert rh inflated
-overlay ./fbert1.feat/stats/zstat1.nii.gz
-overlay-reg ./fbert1.feat/reg/freesurfer/anat2exf.register.dat
-fthresh 2.3 -fmid 3.3 -fslope 1
Visual, Auditory, Motor
Can display any functional data, eg,
zstat, fzstat, cope, pe, etc

## Slide 12: Mapping Automatic Segmentations
$FREESURFER_HOME/FreeSurferColorsLUT.txt
aparc+aseg.mgz
lh.aparc.annot
aseg.mgz

## Slide 13: Mapping Automatic Segmentations
aseg2feat --feat fbert.feat –aseg aparc+aseg
In the functional FOV, creates:
fbert1.feat/reg/freesurfer/aseg+aparc.nii.gz
Create Text Summary Table (nvox, mean cope, std cope, etc)
mri_segstats --seg fbert1.feat/reg/freesurfer/aparc+aseg.nii.gz
--nonempty --ctab-default --in fbert.feat/stats/cope1.nii.gz
--sum fbert1.sum.txt
Can summarize any functional data, eg,
zstat, fzstat, cope, pe, etc

## Slide 14: Make and View ROI
tkmedit bert orig.mgz -aux brain.mgz
-overlay ./fbert1.feat/reg/freesurfer/lh.putamen.nii.gz
-overlay-reg ./fbert1.feat/reg/freesurfer/anat2exf.register.dat
-fthresh 0.5 -seg aparc+aseg.mgz
Make a binary mask of the left putamen:
Note: 12 = Left Putamen,
see $FREESURFER_HOME/FreeSurferColorsLUT.txt
fslmaths
./fbert1.feat/reg/freesurfer/aparc+aseg.nii.gz
-thr 12 -uthr 12
./fbert1.feat/reg/freesurfer/lh.putamen.nii.gz

## Slide 15: Within-Subject, Cross-Run Analysis
Analyze each run with FEAT (dataX.feat)
Combine runs with GFEAT (standard space)
mean_func.nii.gz – avg of example_func in std space
Register each run (not .gfeat) with reg-feat2anat.
dataX.feat/reg/freesurfer/anat2std.register.dat
All runs (X) should be very close
Verify the registration
tkregister2 –mov data.gfeat/mean_func.nii.gz
--reg anat2std.register.dat --surf
Use anat2std.register.dat the way you would anat2exf.register.dat

## Slide 16: Surface-based Group Analysis
mris_preproc --out lh.cope1.nii.gz --target fsaverage --hemi lh
--iv fbert.feat/stats/cope1.nii.gz fbert.feat/reg/freesurfer/anat2exf.register.dat
--iv fgreg.feat/stats/cope1.nii.gz fgreg.feat/reg/freesurfer/anat2exf.register.dat
--iv fsally.feat/stats/cope1.nii.gz fsally.feat/reg/freesurfer/anat2exf.register.dat
--iv fpat.feat/stats/cope1.nii.gz fpat.feat/reg/freesurfer/anat2exf.register.dat
lh.cope1.nii.gz – “volume-encoded surface file”: dim 1974 x 1 x 83 = 163842
dim nframes = number of subjects
Can map any functional data, eg, zstat, fzstat, cope, pe, etc
fsaverage – defines common space (spherical surface)
mri_glmfit (FreeSurfer), randomise (FSL), flame (FSL), melodic (FSL)
Volumes
Registrations

## Slide 17: Practical Data
Sensory-motor study
Blocked Design (15sec OFF, 15 sec ON)
One subject – “bert”
Two runs (TR=3, 85 time points)
FEAT has been run on both runs (FWHM=5)
Combined with GFEAT
  FFx
  One-Sample Group Mean (OSGM)
Actually, all analysis steps already performed!

## Slide 18: Practical
Automatic registration (<5 min)
Manual registration
View FEAT results on subject’s anatomy (aparc+aseg)
View FEAT results with tksurfer
Map aparc+aseg to Functional Space
Verify GFEAT registration
View GFEAT results in volume and on surface
“Higher-Level” analysis with mri_glmfit
  Cross-Run
  Fixed-Effects (FFX), One-Sample Group Mean (osgm)