## Slide 1: FreeSurfer: Failure Modes and Interventions surfer.nmr.mgh.harvard.edu

## Slide 2: Troubleshooting
Segmentation Errors.
Intensity Normalization.
Pial Surface misplacement.
Skull Strip Errors (none on our test set).

## Slide 3: What are the Common Interventions?
Manually edit the wm.mgz to change incorrectly labeled voxels (only for small errors).
Manually edit the brainmask.mgz to erase dura/vasculature.
Adjust watershed parameters to fix large-scale skull-strip errors.
Manually erase/clone regions of skull strip failure.
Control Points – add locations that are in the interior of the white matter and <110 to bring regional wm intensity up.
Use tkregister2 to fix incorrect talairach.xfm

## Slide 4: Troubleshooting – Common Cases (≈98% of surface accurate in about 98% of cases for good data [1])
Symptom: white matter not accurate in wm.mgz
Interventions
  add control points (if wm << 110).
  Expert opts to set intensity thresholds in segmentation (almost never).
  Manually erase/draw wm in wm.mgz
Symptom: skull strip not accurate
Interventions
  Adjust mri_watershed parameters
  Manually erase skull/clone T1.mgz to recover brain
Symptom: surfaces are not accurate.
Interventions:
  Add control points (if white matter << 110).
  Erase dura/blood vessels
  Check topology on ?h.inflated.nofix (if ?h.orig surface doesn’t follow wm.mgz)
[1] Salat, D, 2009. Personal Communication.

## Slide 5
Eye Socket classified as WM due to Skull Strip Failure.
Erase in wm.mgz then run:
recon-all -s <subject> -autorecon2-wm -autorecon3
Troubleshooting: Segmentation Error

## Slide 6
“Hypo-Intensities”
White Matter Lesions
Misclassified as gray matter
Troubleshooting: Segmentation Error
Fill in wm.mgz then run:
recon-all -s <subject> -autorecon2-wm -autorecon3

## Slide 7
Intensity Normalization Failure. Most WM in T1 volume (T1.mgz) should be close to 110. Can fix by editing wm.mgz or adding “Control Points”. Beware partial voluming!
recon-all -s <subject> -autorecon2-cp -autorecon3
Troubleshooting: Intensity Normalization

## Slide 8
Troubleshooting: Skull Strip (very rare now)
brainmask.mgz
orig.mgz
Use “clone” tool to manually correct, or adjust watershed parameters and run (default wsthresh is 25, higher means strip less):
recon-all -skullstrip -wsthresh 35 -clean-bm -no-wsgcaatlas -s <subj>
recon-all -s <subject> -autorecon2 -autorecon3

## Slide 9
Dura or Blood Vessel
White/Gray OK, but
Pial Inaccurate
Troubleshooting: Skull Strip/Pial Surface Error
Dura and GM have extremely similar intensity characteristics on most T1-weighted sequences (but different T2*!). Typical fix: edit the brainmask.mgz to erase dura/blood vessels, and run:
recon-all -s <subject> -autorecon2-pial -autorecon3

## Slide 10: New Morphometry Protocol: Identifying Dura with Multi-echo MP-RAGE
*joint work with Andre van der Kouwe

## Slide 11: Troubleshooting: Topological Defects
Fornix
Pallidum and Putamen
hippocampus
Ventricles and Caudate
Cortical Defects
Holes
Handles
Automatically Fixed

## Slide 12: Topology Correction
BEFORE
AFTER

## Slide 13
Topological defect
Corrected defect
Initial cortical surface
Sagittal view
Coronal view
Automatic Defect Correction
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Automatic Defect Correction
Difference between uncorrected (green) and corrected (red)
Notes: TR=40,TE=20,a=15o, BW=30Hz/voxel

## Slide 15
White Matter
“disconnects”
orig.nofix will be
accurate
Troubleshooting: Topology Fixer Error

## Slide 16: Troubleshooting – Advice
Always look at the data in multiple views and scroll back and forth a few slices – 3D structure is difficult to discern!
If large regions of white matter are significantly darker than 110 (the target white matter intensity for normalization) then try adding control points, but make sure they are in the interior of the white matter.
If the ?h.orig surface misses white matter that is accurately labeled in the wm.mgz or extends into regions where there is no wm in the wm.mgz, then there is an incorrectly fixed topological defect.
Even one or two missing voxels can cause large-scale defects, so very minor editing (e.g. filling in white matter voxels that are holes, or erasing handles) may fix the problem.
Don’t edit too much! This will reduce reliability and is almost never needed. Usually this means you need to start over as you’ve done something wrong (e.g. put control points in the wrong place).

## Slide 17: Processing Stream Order