## Slide 1: Surface-based Group Analysis in FreeSurfer

## Slide 2
Outline
Processing Stages
Command-line Stream
  Assemble Data
  Design/Contrast (GLM Theory)
  Analyze
  Visualize
Interactive/Automated GUI (QDEC)
Correction for multiple comparisons

## Slide 3
Surface-based Study (Thickness)

## Slide 4: Surface-based Measures
Morphometric (eg, thickness)
Functional
PET
MEG/EEG
Diffusion (?) sampled just under the surface

## Slide 5
Processing Stages
Specify Subjects and Surface measures
Assemble Data:
  Resample into Common Space
  Smooth
  Concatenate into one file
Model and Contrasts (GLM)
Fit Model (Estimate)
Correct for multiple comparisons
Visualize

## Slide 6: Intersubject Registration

## Slide 7
Volumetric Interesubject Registration (Affine)
3D Coordinate System
  XYZ, RAS
  MR Intensity
Affine/Linear
  Translate
  Rotate
  Stretch
  Shear
  (12 DOF)
Match Intensity, Voxel-by-Voxel
Problems
Can use nonlinear volumetric (cf CVS)

## Slide 8: Surface-based Intersubject Registration
pial
inflated
superior temporal
calcarine
central
sylvian
anterior
posterior
Curvature
SULCUS (+)
GYRUS (-)
Sheet: 2D Coordinate System (X,Y)
Sphere: 2D Coordinate System ()
Continuous, no cuts

## Slide 9: Surface-based Intersubject Registration
Subject 2
Subject 1
Translate, Rotate, Stretch, Shear (12 DOF)
Match Curvature, Vertex-by-Vertex
Nonlinear Stretching (“Morphing”) allowed (area regularization)
Actually done on sphere
“Spherical Morph”
Curvature “Intensity”
SULCUS (+)
GYRUS (-)
Codes folding pattern

## Slide 10: Surface-based Intersubject Registration
  Gray Matter-to-Gray Matter (it’s all gray matter!)
  Gyrus-to-Gyrus and Sulcus-to-Sulcus
  Some minor folding patterns won’t line up
  Fully automated, no landmarking needed
  Atlas registration is probabilistic, most variable regions get less weight.
  Done in recon-all

## Slide 11: Spatial Smoothing
Why should you smooth?
Might Improve CNR
Improve intersubject registration (functional)
How much smoothing?
Blob-size
Typically 10-20 mm FWHM
Surface smoothing more forgiving than volume-based

## Slide 12: Volume-based Smoothing
  Smoothing is averaging of nearby voxels
7mm FWHM
14mm FWHM

## Slide 13: Volume-based Smoothing
  5 mm apart in 3D
  25 mm apart on surface!
  Kernel much larger
  Averaging with other tissue types (WM, CSF)
  Averaging with other functional areas
14mm FWHM

## Slide 14: Surface-based Smoothing
superior temporal
calcarine
central
sylvian
anterior
posterior
Sheet: 2D Coordinate System (X,Y)
Sphere: 2D Coordinate System ()
  Smoothing is averaging of nearby vertices

## Slide 15: The General Linear Model (GLM)

## Slide 16: GLM Theory
HRF Amplitude
IQ, Height, Weight
Independent Variable
Is Thickness correlated with Age?
Dependent
Variable,
Measurement
x1
x2
y2
y1
Subject 1
Subject 2
Thickness
Age
Of course, you’d
need more then two
subjects …

## Slide 17: Linear Model
Intercept: b
Slope: m
Thickness
Age
x1
x2
y2
y1
System of Linear Equations
y1 = 1*b + x1*m
y2 = 1*b + x2*m
Y = X*
y1
y2
1 x1
1 x2
b
m
=
*
Matrix Formulation
X = Design Matrix
 = Regression Coefficients
= Parameter estimates
= “betas”
= Intercepts and Slopes
= beta.mgh (mri_glmfit)
b
m

Intercept = Offset
mri_glmfit output: beta.mgh

## Slide 18: Hypotheses and Contrasts
Is Thickness correlated with Age?
Does m = 0?
Null Hypothesis: H0: m=0
Intercept: b
Slope: m
Thickness
Age
x1
x2
y2
y1
m= [0 1]*
b
m
 = C*
?
C=[0 1]: Contrast Matrix
b
m

y1
y2
1 x1
1 x2
b
m
=
*
mri_glmfit output: gamma.mgh

## Slide 19: More than Two Data Points
y1 = 1*b + x1*m
y2 = 1*b + x2*m
y3 = 1*b + x3*m
y4 = 1*b + x4*m
y1
y2
y3
y4
1 x1
1 x2
1 x3
1 x4
b
m
=
*
Y = X*
Intercept: b
Slope: m
Thickness
Age
Model Error
Noise
Uncertainty
rvar.mgh
Notes: No matter how many data points you have, there is still only one slope and one intercept.

## Slide 20: t-Test and p-values
 = C*
Y = X*
p-value/significance
value between 0 and 1
closer to 0 means more significant
FreeSurfer stores p-values as –log10(p):
0.1=10-1sig=1, 0.01=10-2sig=2
sig.mgh files
Signed by sign of 
p-value is for an unsigned test

## Slide 21: Two Groups
Do groups differ in Intercept?
Do groups differ in Slope?
Is average slope different than 0?
…
Intercept: b1
Slope: m1
Thickness
Age
Intercept: b2
Slope: m2

## Slide 22: Two Groups
Intercept: b1
Slope: m1
Thickness
Age
Intercept: b2
Slope: m2
y11 = 1*b1 + 0*b2 + x11*m1 + 0*m2
y12 = 1*b1 + 0*b2 + x12*m1 + 0*m2
y21 = 0*b1 + 1*b2 + 0*m1 + x21*m2
y22 = 0*b1 + 1*b2 + 0*m1 + x22*m2
y11
y12
y21
y22
1 0 x11 0
1 0 x12 0
0 1 0 x21
0 1 0 x22
b1
b2
m1
m2
=
*
Y = X*

## Slide 23: Two Groups
Intercept: b1
Slope: m1
Thickness
Age
Intercept: b2
Slope: m2
Do groups differ in Intercept?
Does b1=b2?
Does b1-b2 = 0?
C = [+1 -1 0 0],  = C*
Is average slope different than 0?
Does (m1+m2)/2 = 0?
C = [0 0 0.5 0.5],  = C*
y11
y12
y21
y22
1 0 x11 0
1 0 x12 0
0 1 0 x21
0 1 0 x22
=
*
b1
b2
m1
m2
Y = X*
Do groups differ in Slope?
Does m1=m2?
Does m1-m2=0?
C = [0 0 +1 -1],  = C*
b1
b2
m1
m2


## Slide 24: Surface-based Group Analysis in FreeSurfer
Create your own design matrix and contrast matrices
Create an FSGD File
  FreeSurfer creates design matrix
  You still have to specify contrasts
QDEC
  Limited to 2 discrete variables, 2 levels max
  Limited to 2 continuous variables

## Slide 25
Command-line Processing Stages
Assemble Data (mris_preproc)
  Resample into Common Space
  Smooth
  Concatenate into one file
Model and Contrasts (GLM) (FSGD)
Fit Model (Estimate) (mri_glmfit)
Correct for multiple comparisons
Visualize (tksurfer)
}
recon-all -qcache

## Slide 26: Specifying Subjects
bert
$SUBJECTS_DIR
fred
jenny
margaret …
Subject ID
Notes: Set SUBJECTS_DIR, issue a command (mksubjdirs) to create directory structure. Convert (using mri_convert) data to COR format and store in mri/RRR, run recon-all. Typically, we acquire 3 high-quality T1 volumes to use as input to reconstruction (128-slice sagital, 1 mm in-plane resolution).

## Slide 27: FreeSurfer Directory Tree
bert
bem stats morph mri rgb scripts surf tiff label
orig T1 brain wm aseg
SUBJECTS_DIR environment variable
lh.white
rh.white
lh.thickness
rh.thickness
lh.sphere.reg
rh.sphere.reg
lh.aparc_annnot
rh.aparc_annnot
Subject ID
Notes: Set SUBJECTS_DIR, issue a command (mksubjdirs) to create directory structure. Convert (using mri_convert) data to COR format and store in mri/RRR, run recon-all. Typically, we acquire 3 high-quality T1 volumes to use as input to reconstruction (128-slice sagital, 1 mm in-plane resolution).

## Slide 28: Example: Thickness Study
$SUBJECTS_DIR/bert/surf/lh.thickness
$SUBJECTS_DIR/fred/surf/lh.thickness
$SUBJECTS_DIR/jenny/surf/lh.thickness
$SUBJECTS_DIR/margaret/surf/lh.thickness
…

## Slide 29: FreeSurfer Group Descriptor (FSGD) File
Note: Can specify design matrix explicitly with --design
Simple text file
List of all subjects in the study
Accompanying demographics
Automatic design matrix creation
You must still specify the contrast matrices
Integrated with tksurfer

## Slide 30: FSGD Format
GroupDescriptorFile 1
Class Male
Class Female
Variables Age Weight IQ
Input bert Male 10 100 1000
Input fred Male 15 150 1500
Input jenny Female 20 200 2000
Input margaret Female 25 250 2500
Note: Can specify design matrix explicitly with --design
Class = Group
One Discrete Factor (Gender) with Two Levels (M&F)
Three Continuous Variables: Age, Weight, IQ

## Slide 31: FSGDF  X (Automatic)
DODS – Different Offset, Different Slope
C = [-1 1 0 0 0 0 0 0]
}
Tests for the difference in intercept/offset between groups
1 0 10 0 100 0 1000 0
1 0 15 0 150 0 1500 0
0 1 0 20 0 200 0 2000
0 1 0 25 0 250 0 2500
X =
Male Group
Female Group
Female Age
Male Age
Weight
Age
IQ
C = [ 0 0 -1 1 0 0 0 0]
}
Tests for the difference in age slope between groups

## Slide 32: Factors, Levels, Groups
Each Group/Class:
  Has its own Intercept
  Has its own Slope (for each continuous variable)
NRegressors = NClasses*(NVariables+1)

## Slide 33: Factors, Levels, Groups, Classes
Continuous Variables/Factors: Age, IQ, Volume, etc
Discrete Variables/Factors: Gender, Handedness, Diagnosis
Levels of Discrete :
Handedness: Left and Right
Gender: Male and Female
Diagnosis: Normal, MCI, AD
Group or Class: Specification of All Discrete Factors:
Left-handed Male MCI
Right-handed Female Normal

## Slide 34: Assemble Data: mris_preproc
--fsgd FSGDFile : Specify subjects thru FSGD File
--hemi lh : Process left hemisphere
--meas thickness : $SUBJECTS_DIR/subjectid/surf/hemi.thickness
--target fsaverage : common space is subject fsaverage
--o lh.thickness.mgh : output “volume-encoded surface file”
Lots of other options!
mris_preproc --help
lh.thickness.mgh – file with thickness maps for all subjects  Input to Smoother or GLM

## Slide 35: Surface Smoothing
mri_surf2surf --help
Loads lh.thickness.mgh
2D surface-based smoothing
Specify FWHM (eg, fwhm = 10 mm)
Saves lh.thickness.sm10.mgh
Can be slow (~10-60min)
recon-all -qcache

## Slide 36: mri_glmfit
Reads in FSGD File and constructs X
Reads in your contrasts (C1, C2, etc)
Loads data (lh.thickness.sm10.mgh)
Fits GLM (ie, computes )
Computes contrasts (=C*)
t or F ratios, significances
Significance -log10(p) (.01  2, .001  3)

## Slide 37: mri_glmfit
mri_glmfit
--y lh.thickness.sm10.mgh
--fsgd gender_age.txt
--C age.mat –C gender.mat
--surf fsaverage lh
--cortex
--glmdir lh.gender_age.glmdir
Creates: lh.gender_age.glmdir/
beta.mgh – parameter estimates
rvar.mgh – residual error variance
etc …
age/
sig.mgh – -log10(p), uncorrected
gamma.mgh, F.mgh
gender/
sig.mgh – -log10(p)
gamma.mgh, F.mgh
mri_glmfit --help

## Slide 38
Visualization with tksurfer
View->Configure->Overlay
Threshold:
-log10(p),
Eg, 2=.01
Saturation:
-log10(p),
Eg, 5=.00001
False
Dicovery
Rate
Eg, .01
File->LoadOverlay

## Slide 39
Visualization with tksurfer
File->
Load Group Descriptor File …

## Slide 40: Problem of Multiple Comparisons
p < 0.10
p < 0.01
p < 10-7

## Slide 41: Correction for Multiple Comparisons
Cluster-based
  Monte Carlo simulation
  Permutation Tests
  Surface Gaussian Random Fields (GRF)
    There but not fully tested
False Discovery Rate (FDR) – built into tksurfer and QDEC. (Genovese, et al, NI 2002)

## Slide 42: Clustering
Choose a vertex-wise threshold
  Eg, 2 (p<.01), or 3 (p<.001)
  Sign (pos, neg, abs)
A cluster is a group of connected (neighboring) vertices above threshold
Cluster has a size (area in mm2)
p<.01 (-log10(p)=2)
Negative
p<.0001 (-log10(p)=4)
Negative

## Slide 43: Cluster-based Correction for Multiple Comparisons
Simulate data under Null Hypothesis:
  Synthesize Gaussian noise and then smooth (Monte Carlo)
  Permute rows of design matrix (Permutation, orthog)
Analyze, threshold, cluster, max cluster size
Repeat 10,000 times
Analyze real data, get cluster sizes
P(cluster) = #MaxClusterSize > ClusterSize/10000
mri_glmfit-sim

## Slide 44
QDEC – An Interactive Statistical Engine GUI
Query – Select subjects based on Match Criteria
Design – Specify discrete and continuous factors
Estimate – Fit Model
Contrast – Automatically Generate Contrast Matrices
Interactive – Makes easy things easy (that used to be hard)
…a work in progress
No Query yet
Two Discrete Factors (Two Levels)
Two Continuous Factors
Surface only

## Slide 45
QDEC – Spreadsheet
fsid gender age diagnosis Left-Cerebral-White-Matter-Vol
011121_vc8048 Female 70 Demented 202291
021121_62313-2 Female 71 Demented 210188
010607_vc7017 Female 73 Nondemented 170653
021121_vc10557 Male 75 Demented 142029
020718_62545 Male 76 Demented 186087
020322_vc8817 Male 77 Nondemented 149810
qdec.table.dat – spreadsheet with subject information – spreadsheet can be huge!
Female
Male
gender.levels
Demented
Nondemented
diagnosis.levels
Discrete Factors need a
factorname.level file

## Slide 46: Tutorial
Command-line Stream
  Create an FSGD File for a thickness study
  Age and Gender
  Run
    mris_preproc
    mri_surf2surf
    mri_glmfit
    mri_glmfit-sim
    tksurfer
QDEC – same data set

## Slide 48: Another FSGD Example
GroupDescriptorFile 1
Class MaleRight
Class MaleLeft
Class FemaleRight
Class FemaleLeft
Variables Age
Input bert MaleLeft 10
Input fred MaleRight 15
Input jenny FemaleRight 20
Input margaret FemaleLeft 25
Class = Group
Two Discrete Factors
  Gender: Two Levels (M&F)
  Handedness: Two Levels (L&R)
One Continuous Variable: Age

## Slide 49: Interaction Contrast
GroupDescriptorFile 1
Class MaleRight
Class MaleLeft
Class FemaleRight
Class FemaleLeft
Input bert MaleLeft
Input fred MaleRight
Input jenny FemaleRight
Input margaret FemaleLeft
Two Discrete Factors (no continuous, for now)
  Gender: Two Levels (M&F)
  Handedness: Two Levels (L&R)
Four Regressors (Offsets)
  MR (1), ML (2), FR (3), FL (4)
M
F
R
L
1
4
3
2



3-1)- 4-2)
1+2+ 3-4
C = [-1 +1 +1 -1]


## Slide 50
QDEC GUI
Load QDEC Table File
  List of Subjects
  List of Factors (Discrete and Cont)
Choose Factors
Choose Input (cached):
  Hemisphere
  Measure (eg, thickness)
  Smoothing Level
“Analyze”
  Builds Design Matrix
  Builds Contrast Matrices
  Constructs Human-Readable Questions
  Analyzes
  Displays Results

## Slide 51
Notes: .

## Slide 53: FSGDF X
1 0 10 100 1000
1 0 15 150 1500
0 1 20 200 2000
0 1 25 250 2500
DOSS – Different Offset, Same Slope
X =
C = [-1 1 0 0 0]
#Regressors = Nv+Nc = 3+2=5  Fewer regressors than DODS
DOF = #Rows - #Regressors
Male Class
Female Class
Age for Males and Females
 Same test, different vector
Input:
y
X
C
Notes: .