## Slide 1: Working with FreeSurfer ROIs surfer.nmr.mgh.harvard.edu

## Slide 2: Outline
ROI Studies
  Volumetric/Area
  “Intensity”
Atlas Creation and Application
FreeSurfer ROI Nomenclature
FreeSurfer ROI Atlases
ROI Statistics Files
Separate Talk for Multimodal Integration

## Slide 3: ROI Volume Study
Data courtesy of Drs Marilyn Albert Ron Killiany
Volume of Lateral Ventricle
Lateral Ventricle
Control
Questbl
Converters
AD

## Slide 4: ROI Mean “Intensity” Analysis
Average a point measure over ROI
Individualized ROI critical
MR Intensity (T1)
Thickness, Sulcal Depth
Multimodal
  fMRI intensity
  FA

## Slide 5: ROI Mean “Intensity” Studies
Salat, et al, 2004.
Sigalovsky, et al, 2006
Greve, et al, 2008.
fMRI Noise

## Slide 6: ROI Atlas Creation
Hand label N data sets
  Volumetric: CMA
  Surface Based:
    Desikan/Killiany
    Destrieux
Map labels to common coordinate system
Probabilistic Atlas
  Probability of a label at a vertex/voxel
    Maximum Likelihood (ML) Atlas Labels
  Curvature/Intensity means and stddevs
  Neighborhood relationships
You can create your own atlases

## Slide 7: Automatic Labeling
Transform ML labels to individual subject*
Adjust boundaries based on
  Curvature/Intensity statistics
  Neighborhood relationships
Result: labels are customized to each individual.
* Formally, we compute maximum a posteriori estimate of the labels given the input data

## Slide 8: Validation -- Jackknife
Hand label N Data Sets
Create atlas from (N-1) Data Sets
Automatically label the left out Data Set
Compare to Hand-Labeled
Repeat, Leaving out a different data set each time

## Slide 9
ICBM Atlas
Why not just register to an ROI Atlas?
12 DOF
(Affine)

## Slide 10
Subject 1
Subject 2 aligned with Subject 1
(Subject 1’s Surface)
Problems with Affine (12 DOF) Registration
ROIs need to be individualized.

## Slide 11: Can’t segment on intensity alone

## Slide 12
Markov Random Field: Motivation
What is the probability that cortical gray matter occurs inferior to hippocampus?

## Slide 13
Segmentation: MRF
Preliminary Segmentation

## Slide 14
Segmentation: MRF
Final Segmentation

## Slide 15: FreeSurfer ROI Nomenclature
Segmentation
Color Lookup Table (LUT)
Mask
Parcellation/Annotation
Label

## Slide 16: Segmentation
Volume or surface (usually volume)
Volume-style format (eg, mgz, nii, etc)
Each voxel/vertex has one index
Index into color lookup table (LUT)
  $FREESUFER_HOME/FreeSurferColorLUT.txt
  17 Left-Hippocampus 220 216 20 0
  Index = 17
  Name = Left-Hippocampus
  Red=220, Green=216, Blue=20 (out of 255)
  Statistic = 0 (not really used)
aseg.mgz, aparc+aseg.mgz, aparc.a2005+aseg.mgz, wmparc.mgz

## Slide 17: Segmentation, Continued
Activation Clusters
Thresholded Activity
Clusters as segmentations/annotation
  Each cluster gets its own number/index
  One output of mri_volcluster and mri_surfcluster
Masks
  Binary: 0, 1
  Can be derived by thresholding statistical maps

## Slide 18: Parcellation/Annotation
Surface ONLY
Annotation format (something.annot)
Each vertex has only one label
Format is complicated (and annoying)
?h.aparc.annot, ?h.aparc.a2005.annot

## Slide 19: Label File
Surface or Volume
Simple Text format (usually something.label)
  Two-line header
  Each row as 5 Columns: Vertex X Y Z Statistic
    Vertex – 0-based vertex number
      only applies to surfaces, ignored for volumes
    XYZ – coordinates (in one of many systems)
    Statistic – often ignored
Eg, lh.cortex.label
#label , from subject fsaverage
4
88 -42.261 -81.724 -13.242 0.000000
445 -28.781 -85.827 -16.289 0.000000
446 -39.862 -74.518 -14.432 0.000000
616 -42.856 -74.239 -5.499 0.000000
      Indicates 4 “points” in label

## Slide 20: Label File
Why use a label?
  Volume and Surface
  Easy to draw
  Simple text format

## Slide 21: Creating Label Files
Drawing tools:
  tkmedit
  tksurfer
  QDEC
Deriving from other data
  mris_annotation2label
  mri_volcluster
  mri_surfcluster
  mri_cor2label
  mri_label2label

## Slide 22: Volumetric Segmentation (aseg)
Caudate
Pallidum
Putamen
Amygdala
Hippocampus
Lateral Ventricle
Thalamus
White Matter
Cortex
Not Shown:
Nucleus Accumbens
Cerebellum
Whole Brain Segmentation: Automated Labeling of Neuroanatomical Structures in the Human Brain, Fischl, B., D.H. Salat, E. Busa, M. Albert, M. Dieterich, C. Haselgrove, A. van der Kouwe, R. Killiany, D. Kennedy, S. Klaveness, A. Montillo, N. Makris, B. Rosen, and A.M. Dale, (2002). Neuron, 33:341-355.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Volumetric Segmentation Atlas Description
39 Subjects
14 Male, 25 Female
Ages 18-87
  Young (1-22): 10
  Mid (40-60): 10
  Old Healthy (69+): 8
  Old Alzheimer's (68+): 11
Siemens 1.5T Vision (Wash U)
Whole Brain Segmentation: Automated Labeling of Neuroanatomical Structures in the Human Brain, Fischl, B., D.H. Salat, E. Busa, M. Albert, M. Dieterich, C. Haselgrove, A. van der Kouwe, R. Killiany, D. Kennedy, S. Klaveness, A. Montillo, N. Makris, B. Rosen, and A.M. Dale, (2002). Neuron, 33:341-355.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Automatic Surface Parcellation: Desikan/Killiany Atlas
Precentral Gyrus
Postcentral Gyrus
Superior Temporal Gyrus
An automated labeling system for subdividing the human cerebral cortex on MRI scans into gyral based regions of interest, Desikan, R.S., F. Segonne, B. Fischl, B.T. Quinn, B.C. Dickerson, D. Blacker, R.L. Buckner, A.M. Dale, R.P. Maguire, B.T. Hyman, M.S. Albert, and R.J. Killiany, (2006). NeuroImage 31(3):968-80.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: Desikan/Killiany Atlas
40 Subjects
14 Male, 26 Female
Ages 18-87
30 Nondemented
10 Demented
Siemens 1.5T Vision (Wash U)
An automated labeling system for subdividing the human cerebral cortex on MRI scans into gyral based regions of interest, Desikan, R.S., F. Segonne, B. Fischl, B.T. Quinn, B.C. Dickerson, D. Blacker, R.L. Buckner, A.M. Dale, R.P. Maguire, B.T. Hyman, M.S. Albert, and R.J. Killiany, (2006). NeuroImage 31(3):968-80.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26: Automatic Surface Parcellation: Destrieux Atlas
Automatically Parcellating the Human Cerebral Cortex, Fischl, B., A. van der Kouwe, C. Destrieux, E. Halgren, F. Segonne, D. Salat, E. Busa, L. Seidman, J. Goldstein, D. Kennedy, V. Caviness, N. Makris, B. Rosen, and A.M. Dale, (2004). Cerebral Cortex, 14:11-22.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27: Automatic Surface Parcellation: Destrieux Atlas
Automatically Parcellating the Human Cerebral Cortex, Fischl, B., A. van der Kouwe, C. Destrieux, E. Halgren, F. Segonne, D. Salat, E. Busa, L. Seidman, J. Goldstein, D. Kennedy, V. Caviness, N. Makris, B. Rosen, and A.M. Dale, (2004). Cerebral Cortex, 14:11-22.
58 Parcellation Units
12 Subjects
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28: Derived ROIs
Combined Volume-Surface segmentation
  aparc+aseg.mgz, a2005.aparc+aseg.mgz
White Matter Parcellation
  wmparc.mgz

## Slide 29: Combined Segmentation
aparc+aseg
aseg
aparc
Use ROI volume as computed from aparc (more accurate)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 30: Gyral White Matter Segmentation
Nearest Cortical Label
to point in White Matter
aparc+aseg
wmparc
+
+
Notes: <number>
<footer>
<header>
<date/time>

## Slide 31: ROI Statistic Files
Simple text files
Volume and Surface ROIs (different formats)
Automatically generated: aseg.stats, lh.aparc.stats, etc
Combine multiple subjects into one table with asegstats2table or aparcstats2table (then import into excel).
You can generate your own with either
  mri_segstats
  mris_anatomical_stats

## Slide 32: Brain, Gray, and White Matter, Intracranial Volumes
Brain – gray matter + white matter + ventricles + hypointensities + hyperintensities
Total Gray – cortical + subcortical gray
Cortical Gray – volume between white and pial excluding non-cortical regions.
Intracranial volume (ICV), estimated Total Intracranial Volume (eTIV)

## Slide 33: Segmentation Stats File
Index SegId NVoxels Volume_mm3 StructName Mean StdDev Min Max Range
1 2 255076 255076.0 Left-Cerebral-White-Matter 101.5872 7.9167 34.0000 148.0000 114.0000
2 3 266265 266265.0 Left-Cerebral-Cortex 75.3682 9.4016 28.0000 152.0000 124.0000
3 4 5855 5855.0 Left-Lateral-Ventricle 37.7920 10.9705 20.0000 88.0000 68.0000
4 5 245 245.0 Left-Inf-Lat-Vent 56.4091 9.5906 26.0000 79.0000 53.0000
5 7 16357 16357.0 Left-Cerebellum-White-Matter 91.2850 4.8989 49.0000 106.0000 57.0000
6 8 60367 60367.0 Left-Cerebellum-Cortex 76.3620 9.5724 26.0000 135.0000 109.0000
7 10 7460 7460.0 Left-Thalamus-Proper 91.3778 7.4668 43.0000 108.0000 65.0000
8 11 3133 3133.0 Left-Caudate 78.5801 8.2886 42.0000 107.0000 65.0000
9 12 5521 5521.0 Left-Putamen 86.9680 5.5752 66.0000 106.0000 40.0000
10 13 1816 1816.0 Left-Pallidum 97.7162 3.4302 79.0000 106.0000 27.0000
11 14 852 852.0 3rd-Ventricle 41.9007 11.8230 22.0000 69.0000 47.0000
12 15 1820 1820.0 4th-Ventricle 39.7053 10.6407 20.0000 76.0000 56.0000
13 16 25647 25647.0 Brain-Stem 85.2103 8.2819 38.0000 106.0000 68.0000
14 17 4467 4467.0 Left-Hippocampus 77.6346 7.5845 45.0000 107.0000 62.0000
15 18 1668 1668.0 Left-Amygdala 74.5104 5.8320 50.0000 94.0000 44.0000
16 24 1595 1595.0 CSF 52.1348 11.6113 29.0000 87.0000 58.0000
Index: nth Segmentation in stats file
SegId: index into lookup table
NVoxels: number of Voxels/Vertices in segmentation
StructName: Name of structure from LUT
Mean/StdDev/Min/Max/Range: intensity across ROI
Eg: aseg.stats, wmparc.stats (in subject/stats)
created by mri_segstats

## Slide 34: Parcellation Stats File
StructName: Name of structure/ROI
NumVert: number of vertices in ROI
SurfArea: Surface area in mm2
GrayVol: volume of gray matter (surface-based)
ThickAvg/ThickStd – average and stddev of thickness in ROI
MeanCurv – mean curvature
GausCurv – mean gaussian curvature
FoldInd – folding index
CurvInd – curvature index
Eg, lh.aparc.stats, lh.a2005s.aparc.stats
created by mris_anatomical_stats
StructName NumVert SurfArea GrayVol ThickAvg ThickStd MeanCurv GausCurv FoldInd CurvInd
unknown 10863 7151 13207 1.776 1.629 0.121 0.107 383 50.8
bankssts 1222 830 2290 2.711 0.559 0.112 0.027 10 1.3
caudalanteriorcingulate 830 585 1459 2.474 0.569 0.128 0.020 10 0.7
caudalmiddlefrontal 2509 1658 4979 2.653 0.567 0.125 0.035 27 3.5
corpuscallosum 2124 1340 569 0.489 0.631 0.151 0.110 87 8.0
cuneus 2737 1706 3086 1.741 0.509 0.162 0.065 52 8.0
entorhinal 495 330 1685 3.150 0.753 0.149 0.187 15 1.5
fusiform 3878 2638 7887 2.627 0.724 0.137 0.046 57 6.7

## Slide 35: Exporting Stats Files
Convert stats files from a group of subjects into a single table that can be loaded into a spreadsheet.
asegstats2table
aparcstats2table

## Slide 36: Summary
Atlases: Probabilistic
ROIs are Individualized
Volume and Surface
Derived
Measures for Studies
  Volume, Area
  Intensity, Thickness, Curvature
Multimodal Applications
FreeSurfer Nomenclature
  Segmentation, LUT, Parcellation

## Slide 37: Tutorial
Simultaneously load:
  aparc+aseg.mgz (tkmedit)
  aparc.annot (tksurfer)
  FreeSurferColorLUT.txt
View Individual Stats Files
Group Table
  Create
  Load into spreadsheet