## Slide 1: Introduction to MR Physics for Non-Physicists
André J. W. van der Kouwe
Athinoula A. Martinos Center, Massachusetts General Hospital

## Slide 2: Behaviour of spins in magnetic field

## Slide 3: Source of signal in human MRI is water
Human body is 60%/55% water (brain 75% - 95%)
Water molecule contains two hydrogen atoms
Hydrogen nuclei (protons) have charge +1 and spin ½
Charge on a spinning sphere is a flow of current in a loop and generates a magnetic field (Biot-Savart law) called a magnetic dipole
John Blamire, http://www.brooklyn.cuny.edu; http://www.labwater.com

## Slide 4
Magnetic Resonance
Hydrogen nuclei (magnetic dipoles) behave like compass needles in a fixed external magnetic field (B0)
A compass needle oscillates as it comes to rest in the external field
Oscillating magnetic dipoles emit radio waves - this is the MR signal
An external magnetic field (B1) at the right frequency drives the oscillation
Lars Hanson's Compass Model
Danish Research Centre for Magnetic Resonance (DRMCR)

## Slide 5: Magnetic moment precesses about external magnetic field at Larmor frequency
If perturbed, spins precess about direction of external magnetic field
They precess at the “Larmor” frequency (f)
f = γB0 where γ is gyromagnetic ratio 42.576 MHz/T
After a time (T1) the spins realign themselves with the magnetic field
T1 is the spin-lattice or longitudinal relaxation time
As they “relax”, the spins emit radio waves at the Larmor frequency
http://hyperphysics.phy-astr.gsu.edu

## Slide 7: Design of MR scanner

## Slide 8: Scanner components
Main magnet generates very strong and uniform field
Gradient coils (X, Y and Z) encode spatial information
Radio frequency transmit coil perturbs spins
Radio frequency receive coil(s) receive signal from relaxing spins
http://www.magnet.fsu.edu/education/tutorials/magnetacademy/mri/

## Slide 9: Main magnet
Main magnet is superconducting
Niobium-tin/titanium superconducts at temperature of liquid He (4.2 K)
Cooled magnet is “ramped up” to field i.e. energy is stored in magnet
Current continues to flow almost indefinitely (almost zero resistance)
Therefore magnet is “always on”
If helium level becomes too low, magnet quenches i.e. helium boils off, superconductor becomes resistive, energy dissipated as heat
Emergency quench button raises temperature of helium slightly and causes a controlled quench (1700 dm3)
Helium is a limited resource (helium can’t be synthesized like oil)

## Slide 10: Magnetic field gradients
Gradients are resistive coils that slightly alter the main magnetic field
Gradients add to or subtract from the main magnetic field
http://www.magnet.fsu.edu/education/tutorials/magnetacademy/mri/
y
x
z

## Slide 11: Magnetic field gradients
Gradients are resistive coils that slightly alter the main magnetic field
Gradients add to or subtract from the main magnetic field
Gx
positive x-gradient
direction of bore (z)
x
45 mT/m (peak)
200 mT/m/ms (maximum slew)
(or 225 μs to peak)

## Slide 12: Magnetic field gradients
Gradients are resistive coils that slightly alter the main magnetic field
Gradients add to or subtract from the main magnetic field
Gx
negative x-gradient
direction of bore (z)
x
45 mT/m (peak)
200 mT/m/ms (maximum slew)
(or 225 μs to peak)

## Slide 13: Magnetic field gradients
Gradients are resistive coils that slightly alter the main magnetic field
Gradients add to or subtract from the main magnetic field
positive z-gradient
direction of bore (z)
x
Gz

## Slide 14: Magnetic field gradients
Gradients are resistive coils that slightly alter the main magnetic field
Gradients add to or subtract from the main magnetic field
Gz
negative z-gradient
direction of bore (z)
x

## Slide 15: Spin behaviour and relaxation times

## Slide 16
Spins release energy to environment (T1 relaxation)
Environment can supply energy (RF excitation)
Timescale for relaxation of longitudinal magnetization is T1 (e.g. 1 s)
T1 (spin-lattice) relaxation
Nuclei in liquid collide (almost) with one another due to thermal agitation
Consider compass needles in a tumble dryer – individual compasses don’t reach a steady state but the combined distribution quickly does
The “lattice” is the environment
No field
Fixed B0 field
RF excitation
Introduction to MRI Techniques, Lars Hanson, DRCMR

## Slide 17
T2 (spin-spin) relaxation
T2 is the spin-spin or transverse relaxation time
Spins exchange energy with one another (local field variations)
Transverse magnetization decays because spins dephase (but refocusing can be used to reverse dephasing and elicit an echo)
Dephasing can also be caused by field inhomogeneity (poor shim)
Contribution is T2' (property of shim, voxel size etc.)
Like resistors in parallel:
1 / T2* = 1 / T2 + 1 / T2'
T2* relaxation

## Slide 18
Bloch equations / simulator
Bloch equations describe the macroscopic nuclear magnetization M = (Mx, My, Mz) given the relaxation times T1 and T2
Mxy or transverse magnetization induces the observed signal
Danish Research Centre for Magnetic Resonance

## Slide 19: MR-PET combination: Biograph mMR
Simultaneous MR and PET imaging
PET detectors use APDs instead of PMTs to function in magnetic field
Front view
Back view
Ciprian Catana, MGH; Siemens

## Slide 20
Ciprian Catana, MGH; Siemens

## Slide 21: Connectome gradients
High peak gradient strength (Gmax = 300 mT/m vs. standard 45 mT/m)
Enables diffusion imaging with high b-values at low echo times
(b-value scales with Gmax, SNR decreases exponentially with TE)
Power 4 x 2250V/951A (~8.5 MW) (cmp. 2000V/625A ~1.25 MW)
Connectom Skyra
MGH/Siemens (NIH project with UCLA)

## Slide 22
Current 4 x 951A per axis
Connectome gradients
MGH/Siemens (NIH project with UCLA)

## Slide 23
Gmax = 40 mT/m
Gmax = 100 mT/m
Gmax = 300 mT/m
TE = 100 ms
TE = 66 ms
TE = 54 ms
Connectome gradients
Tractography at b = 5000 s/mm2
Julien Cohen-Adad, MGH (ISMRM 2012, 694)
Notes: similar across gradient strength, with overall better consistency for the G100 and G300.
recovering tracts in the cc for G=300 not seen at G=100. Lower SNR at center of the brain due to lower coil sensitivity at the center.
some tracts are more consistently reconstructed at G300, unseen at G100

## Slide 24: Pulse sequences

## Slide 25
RF
ADC
X grad
Y grad.
Z grad.
ME-MPRAGE pulse sequence
Encode line: excitation – measurement – recovery/spoiling
7.7 ms
0 ms

## Slide 26
RF
ADC
X grad
Y grad.
Z grad.
ME-MPRAGE pulse sequence
Encode slice: inversion – phase encoding (loop over lines) – recovery
1 s
0 ms

## Slide 27
RF
ADC
X grad
Y grad.
Z grad.
ME-MPRAGE pulse sequence
Encode volume: loop over slices
32 s
0 ms

## Slide 28: Resources
http://www.e-mri.org
http://www.cis.rit.edu/htbooks/mri/
http://www.drcmr.dk/MR