## Slide 1: Introduction to Diffusion MRI processing
Lilla Zöllei

## Slide 2: dt_recon
Required Arguments:
--i invol
--s subjectid
--o outputdir
Example: dt_recon --i
dt_recon --i 6-1025.dcm --s M111 --o dti
Notes: Performs DTI reconstruction from the DWI in the input dicom file. Gets gradient directions and bvalues from values
found in the dicom file see $FREESURFER_HOME/diffusion/mgh-dti-seqpack/README.
Similar to all other packages.

## Slide 3: Main processing steps
# Eddy current and motion correction
  (FSL eddy_correct)
# Tensor fitting
  tensor.nii, eigvals.nii. eigvec?.nii
  set of scalar maps: adc, fa, ra, vr, ivc
# Registration to anatomical space
  (FSL flirt to lowb)
# Mapping mask, FA to Talairach space
Notes: adc.nii -- apparent diffusion coefficient
fa.nii -- fractional anisotropy
ra.nii -- relative anisotropy
vr.nii -- volume ratio
ivc.nii -- intervoxel correlation

## Slide 4: Other Arguments (Optional)
--b bvals bvecs
--info-dump infodump.dat
  use info dump created by unpacksdcmdir or dcmunpack
--ecref TP
  use TP as 0-based reference time points for EC
--no-ec
  turn off eddy/motion correction
--no-reg
  do not register to subject or resample to talairach
--no-tal
  do not resample FA to talairch space
--sd subjectsdir
  specify subjects dir (default env SUBJECTS_DIR)
--eres-save
  save resdidual error (dwires and eres)
--pca
  run PCA/SVD analysis on eres (saves in pca-eres dir)
--prune_thr thr
  set threshold for masking (default is FLT_MIN)
--debug
  print out lots of info
--version
  print version of this script and exit
--help
  voluminous bits of wisdom

## Slide 5: The diffusion process
http://pubs.niaaa.nih.gov/publications/arh27-2/146-152.htm
Notes: Can be encoded by diffusion matrices  DTI if Gaussian assumption is made.

## Slide 6: Examples of scalar maps
FA: fractional anisotropy (fiber density, axonal diameter, myelination in WM)
RA: relative anisotropy
VR: volume ratio
IVC: inter-voxel correlation (diffusion orientation agreement in neighbors)
ADC: apparent diffusion coefficient (magnitude of diffusion; low value  organized tracts)
RD: radial diffusivity
AD: axial diffusivity
…
Notes: Most interest: anisotropy and diffusivity
FA: fiber density, axonal diameter, myeleination in WM
ADC: magnitude of diffusion (of water molecules) within cerebral tissue. A low value for ADC indicates that the cortical white matter tracts are organized (good), while a high value for ADC indicates that these tracts are disorganized (bad)
IVC: This is the degree to which diffusion in neighboring voxels has a common orientation (Pfefferbaum et al. 2000b). This measure is similar to FA but views coherence on a larger spatial, voxel–to–voxel scale (in contrast with FA’s intravoxel scale).

## Slide 7: FA

## Slide 8
ADC

## Slide 9: IVC

## Slide 10: Tractography examples
Trackvis and Diffusion Toolkit (http://www.trackvis.org/)
Notes: We have richer information in the data. One way to represent it is to draw streamlines / tractography relying on directional information.

## Slide 11
Notes: We have tool to manually isolate certain fibers.

## Slide 12: CST on (color) FA map

## Slide 13: END

## Slide 14
Stages:
1. Convert dicom to nifti (creates dwi.nii)
2. Eddy current and motion correction using FSLs eddy_correct,
creates dwi-ec.nii. Can take 1-2 hours.
3. DTI GLM Fit and tensor construction. Includes creation of:
tensor.nii -- maps of the tensor (9 frames)
eigvals.nii -- maps of the eigenvalues
eigvec?.nii -- maps of the eigenvectors
adc.nii -- apparent diffusion coefficient
fa.nii -- fractional anisotropy
ra.nii -- relative anisotropy
vr.nii -- volume ratio
ivc.nii -- intervoxel correlation
lowb.nii -- Low B
bvals.dat -- bvalues
bvecs.dat -- directions
Also creates glm-related images:
beta.nii - regression coefficients
eres.nii - residual error (log of dwi intensity)
rvar.nii - residual variance (log)
rstd.nii - residual stddev (log)
dwires.nii - residual error (dwi intensity)
dwirvar.nii - residual variance (dwi intensity)
4. Registration of lowb to same-subject anatomical using
FSLs flirt (creates mask.nii and register.dat)
5. Map FA to talairach space (creates fa-tal.nii)
Example usage:
dt_recon --i 6-1025.dcm --s M87102113 --o dti

## Slide 15: After dt_recon
# Check registration
tkregister2 --mov dti/lowb.nii --reg dti/register.dat \
--surf orig --tag
# View FA on the subject's anat:
tkmedit M87102113 orig.mgz -overlay dti/fa.nii \
-overlay-reg dti/register.dat
# View FA on fsaverage
tkmedit fsaverage orig.mgz -overlay dti/fa-tal.nii
# Group/Higher level GLM analysis:
# Concatenate fa from individuals into one file
# Make sure the order agrees with the fsgd below
mri_concat */fa-tal.nii --o group-fa-tal.nii
# Create a mask:
mri_concat */mask-tal.nii --o group-masksum-tal.nii --mean
mri_binarize --i group-masksum-tal.nii --min .999 --o group-mask-tal.nii
# GLM Fit
mri_glmfit --y group-fa-tal.nii --mask group-mask-tal.nii\
--fsgd your.fsgd --C contrast --glm groupanadir