## Slide 1: Working with FreeSurfer ROIs surfer.nmr.mgh.harvard.edu
Notes: 30 minute talk

## Slide 2: Outline
FreeSurfer ROI Terminology
ROI Statistics Files
ROI Studies
  Volumetric/Area
  “Intensity”
FreeSurfer ROI Atlases
Atlas Creation and Application
Notes: ROI = Region of Interest; Talk is going to cover the two ways to analyze an ROI, etc.

## Slide 3: FreeSurfer ROI Terminology
ROI = Region Of Interest
which can include:
  Segmentation (i.e. subcortical)
  Parcellation/Annotation
  Clusters, Masks (from sig.nii, fMRI)
  Label you created

## Slide 4: Segmentation
Volume or surface (usually volume)
Volume-style format (eg, mgz, nii, etc)
Each voxel/vertex has one index (number ID)
Index List found in color lookup table (LUT)
  $FREESUFER_HOME/FreeSurferColorLUT.txt
  17 Left-Hippocampus 220 216 20 0
  Index = 17
  Name = Left-Hippocampus
  Red=220, Green=216, Blue=20 (out of 255)
  Alpha = 0 (not really used)
aseg.mgz, aparc+aseg.mgz, aparc.a2005+aseg.mgz, wmparc.mgz
Notes: segmentation term used for many things
The index ID is just to keep track of all the different structures. Each must be a unique color.
ctx- prefix for cortical parcellations; wm- prefix for wm parcellations
will look at color lut in tutorial (has many more regions than you’ve seen in the seg and parc volumes)
if want to create own label, copy table to own space and add uniqu ID and color

## Slide 5: Parcellation/Annotation
Surface ONLY
Annotation format (something.annot)
Each vertex has only one label/index
Index List also found in color lookup table (LUT)
  $FREESUFER_HOME/FreeSurferColorLUT.txt
?h.aparc.annot, ?h.aparc.a2005.annot
Notes: ctx- prefix for cortical parcellations; wm- prefix for wm parcellations

## Slide 6: Clusters
Activation Clusters
Thresholded Activity
Clusters (significance map; functional activation)
  One output of mri_volcluster and mri_surfcluster
  segmentations or annotation (volume vs. surface)
  Each cluster gets its own number/index
Masks (another type of segmentation)
    Binary: 0, 1
    Can be derived by thresholding statistical maps
Notes: -Clusters are blobs seen in signifcance maps and funtional activation.
-next slide explains commands in freesurfer that create these clusters. volcluster  uses thresholded voxel value; surfcluster  uses intensity vertex value
-can also create mask that assigns voxels/vertices one of 2 values: off or on; Mask out = to see only a certain area. Similar to clusters just created differently.

## Slide 7: Clusters
mri_volcluster
  contiguous voxels (row, col, slice) that meet threshold criteria
  min # of voxels
mri_surfcluster
  intensity must fall within threshold
  part of contiguous set of vertices where surface area is greater than certain minimum
  *many more options; see --help
Notes: -mri_volcuster may require a certain number of voxels to create a cluster
-vertex intensity
-help file shows the many options to set these thresholds as well as other options
-can always ask us to add options

## Slide 8: Clusters
Activation Clusters
Thresholded Activity
Clusters (significance map; functional activation)
  One output of mri_volcluster and mri_surfcluster
  segmentations or annotation (volume vs. surface)
  Each cluster gets its own number/index
Masks (another type of segmentation)
    Binary: 0, 1
    Can be derived by thresholding statistical maps
Notes: -Clusters are blobs seen in signifcance maps and funtional activation.
-next slide explains commands in freesurfer that create these clusters. volcluster  uses thresholded voxel value; surfcluster  uses intensity vertex value
-can also create mask that assigns voxels/vertices one of 2 values: off or on; Mask out = to see only a certain area. Similar to clusters just created differently.

## Slide 9: Label File
  Easy to draw
  Use ‘Select Voxels’ Tool in tkmedit
  Simple text format
In Volume
On Surface
Notes: -click on vertices in tksurfer and ask it to connect those to create label

## Slide 10: Creating Label Files
Drawing tools:
  tkmedit
  tksurfer
  QDEC
Deriving from other data
  mris_annotation2label: cortical parcellation broken into units
  mri_volcluster: create cluster in volume
  mri_surfcluster: create cluster on surface
  mri_cor2label: a volume/segmentation made into a label
  mri_label2label: label from one space mapped to another
Notes: annotation2label = aparc areas made into label format;
cor2label = a volume/segmentation made into a label;
label2label = map a label from one subject to another
-you can merge regions or divide regions in tksurfer

## Slide 11: Label File
Surface or Volume
Simple Text format (usually something.label)
  Each row as 5 Columns: Vertex X Y Z Statistic
    Vertex – 0-based vertex number
      only applies to surfaces, ignored for volumes
    XYZ – coordinates (in one of many systems)
    Statistic – often ignored
Eg, lh.cortex.label
#label , from subject fsaverage
4
88 -42.261 -81.724 -13.242 0.000000
445 -28.781 -85.827 -16.289 0.000000
446 -39.862 -74.518 -14.432 0.000000
616 -42.856 -74.239 -5.499 0.000000
      Indicates 4 “points” in label
Notes: -points as in how many vertex points were used to make the label
-left column is vertex id# followed by xyz coordinate
-statistic ignored; used for brodman area labels where it represents the probability

## Slide 12: ROI Statistic Files
Simple text files
Volume and Surface ROIs (different formats)
Automatically generated: aseg.stats, lh.aparc.stats, etc
Combine multiple subjects into one table with asegstats2table or aparcstats2table (then import into excel).
You can generate your own with either
  mri_segstats (volume)
  mris_anatomical_stats (surface)
    * use -l for label file

## Slide 13: ROI Summaries:
$SUBJECTS_DIR/subjid/stats
aseg.stats – volume summaries
?h.aparc.stats – desikan/killiany atlas summaries
?h.aparc.a2005s.stats – destrieux atlas summaries
wmparc.stats – volume summaries
_______________________________________________
aseg:
volumes of subcortical structures (mm3)
aparc:
thickness of cortical parcellation structures (mm)
total white matter volume (mm3)
number of vertices in cortex
surface area of cortex (mm2)

## Slide 14: Volume (Segmentation) Stats File
Index SegId NVoxels Volume_mm3 StructName Mean StdDev Min Max Range
1 2 255076 255076.0 Left-Cerebral-White-Matter 101.5872 7.9167 34.0000 148.0000 114.0000
2 3 266265 266265.0 Left-Cerebral-Cortex 75.3682 9.4016 28.0000 152.0000 124.0000
3 4 5855 5855.0 Left-Lateral-Ventricle 37.7920 10.9705 20.0000 88.0000 68.0000
4 5 245 245.0 Left-Inf-Lat-Vent 56.4091 9.5906 26.0000 79.0000 53.0000
5 7 16357 16357.0 Left-Cerebellum-White-Matter 91.2850 4.8989 49.0000 106.0000 57.0000
6 8 60367 60367.0 Left-Cerebellum-Cortex 76.3620 9.5724 26.0000 135.0000 109.0000
7 10 7460 7460.0 Left-Thalamus-Proper 91.3778 7.4668 43.0000 108.0000 65.0000
8 11 3133 3133.0 Left-Caudate 78.5801 8.2886 42.0000 107.0000 65.0000
9 12 5521 5521.0 Left-Putamen 86.9680 5.5752 66.0000 106.0000 40.0000
10 13 1816 1816.0 Left-Pallidum 97.7162 3.4302 79.0000 106.0000 27.0000
11 14 852 852.0 3rd-Ventricle 41.9007 11.8230 22.0000 69.0000 47.0000
12 15 1820 1820.0 4th-Ventricle 39.7053 10.6407 20.0000 76.0000 56.0000
13 16 25647 25647.0 Brain-Stem 85.2103 8.2819 38.0000 106.0000 68.0000
14 17 4467 4467.0 Left-Hippocampus 77.6346 7.5845 45.0000 107.0000 62.0000
15 18 1668 1668.0 Left-Amygdala 74.5104 5.8320 50.0000 94.0000 44.0000
16 24 1595 1595.0 CSF 52.1348 11.6113 29.0000 87.0000 58.0000
Index: nth Segmentation in stats file
SegId: index into lookup table
NVoxels: number of Voxels/Vertices in segmentation
StructName: Name of structure from LUT
Mean/StdDev/Min/Max/Range: intensity across ROI
Eg: aseg.stats, wmparc.stats (in subject/stats)
created by mri_segstats
Notes: Volume stats and Intensity stats
there is a partial volume correction done for these stats

## Slide 15: Cortical, Gray, White, Intracranial Volumes
Also in aseg.stats header:
# Measure lhCortex, lhCortexVol, Left hemisphere cortical gray matter volume, 192176.447567, mm^3
# Measure rhCortex, rhCortexVol, Right hemisphere cortical gray matter volume, 194153.9526, mm^3
# Measure Cortex, CortexVol, Total cortical gray matter volume, 386330.400185, mm^3
# Measure lhCorticalWhiteMatter, lhCorticalWhiteMatterVol, Left hemisphere cortical white matter volume, 217372.890625, mm^3
# Measure rhCorticalWhiteMatter, rhCorticalWhiteMatterVol, Right hemisphere cortical white matter volume, 219048.187500, mm^3
# Measure CorticalWhiteMatter, CorticalWhiteMatterVol, Total cortical white matter volume, 436421.078125, mm^3
# Measure SubCortGray, SubCortGrayVol, Subcortical gray matter volume, 182006.000000, mm^3
# Measure TotalGray, TotalGrayVol, Total gray matter volume, 568336.400185, mm^3
# Measure SupraTentorial, SupraTentorialVol, Supratentorial volume, 939646.861571, mm^3
# Measure IntraCranialVol, ICV, Intracranial Volume, 1495162.656130, mm^3
lhCortex, rhCortex, Cortex – surface-based measure of cortical gray matter volume
lhCorticalWhiteMatter, … – surface-based measure of cortical white matter volume
SubCortGray – volume-based measure of subcortical gray matter
TotalGray – Cortex + Subcortical gray
SupraTentorial – Cortex + CorticalWhiteMatter + Subcortical gray
IntraCranialVol – estimated Total Intracranial vol (eTIV)
http://surfer.nm.mgh.harvard.edu/fswiki/eTIV
Notes: Cortex – volume between white and pial surfaces excluding non-cortical regions for whole brain (per hemi also available).
CorticalWhiteMatter – volume within white surface excluding non-cortical regions for whole brain (per hemi also available).
Supratentorial Volume – everything above the tentorium within pial surface + subcortical
etiv wiki

## Slide 16: Getting Stats into Table Format
Organize stats files from a group of subjects into a single text file
asegstats2table \  Command name
--subjects 001 002 003 \  List subjects to include
--meas volume \  vol or mean intensity of struct
--tablefile asegstats.txt  text output file
asegstats.txt created in SUBJECTS_DIR

## Slide 17: Import Text File into Spreadsheet
File > Open
Select asegstats.txt
Choose delimited by Space

## Slide 18: Surface (Parcellation) Stats File
StructName: Name of structure/ROI
NumVert: number of vertices in ROI
SurfArea: Surface area in mm2
GrayVol: volume of gray matter
ThickAvg/ThickStd – average and stddev of thickness in ROI
MeanCurv – mean Gaussian curvature
GausCurv – Gaussian curvature
FoldInd – folding index
CurvInd – curvature index
Eg, lh.aparc.stats, lh.a2005s.aparc.stats
created by mris_anatomical_stats
StructName NumVert SurfArea GrayVol ThickAvg ThickStd MeanCurv GausCurv FoldInd CurvInd
unknown 10863 7151 13207 1.776 1.629 0.121 0.107 383 50.8
bankssts 1222 830 2290 2.711 0.559 0.112 0.027 10 1.3
caudalanteriorcingulate 830 585 1459 2.474 0.569 0.128 0.020 10 0.7
caudalmiddlefrontal 2509 1658 4979 2.653 0.567 0.125 0.035 27 3.5
corpuscallosum 2124 1340 569 0.489 0.631 0.151 0.110 87 8.0
cuneus 2737 1706 3086 1.741 0.509 0.162 0.065 52 8.0
entorhinal 495 330 1685 3.150 0.753 0.149 0.187 15 1.5
fusiform 3878 2638 7887 2.627 0.724 0.137 0.046 57 6.7
Notes: meancurv is mean Gaussian curvature which is min+max/2
GausCurv is Gaussian curvature which is min*max
folding and curv index are from Van Essen paper implemented for compatibility but probably not useful

## Slide 19: Parcellation Stats
Also in ?h.aparc.stats header:
# Measure Cortex, NumVert, Number of Vertices, 129292, unitless
# Measure Cortex, SurfArea, Surface Area, 84209.5, mm^2
# Measure Cortex, MeanThickness, Mean Thickness, 2.29807, mm
Total Number of Vertices – same for white and pial
Total Surface Area – white surface
Total Mean Thickness – between white and pial
Notes: surface area uses white just out of convention
# vertices same between white and pial

## Slide 20: Getting Stats into Table Format
aparcstats2table \  Command name
--subjects 001 002 003 \  List subjects to include
--hemi rh \  Which hemisphere
--meas volume \  volume, thickness, or area
--tablefile rh.aparc.vol.txt  text output file
rh.aparc.vol.txt created in SUBJECTS_DIR
“Gray Vol”, “Avg Thick”, or “Surf Area” of structure

## Slide 21: ROI Studies
Volumetric/Area
  size; number of units that make up the ROI
“Intensity”
  average values at point measures (voxels or vertices) that make up the ROI
Notes: ROI = Region of Interest; Talk is going to cover the two ways to analyze an ROI, etc.

## Slide 22: ROI Volume Study
Data courtesy of Drs Marilyn Albert & Ron Killiany
Volume of Lateral Ventricle
Lateral Ventricle
Control
Questbl
Converters
AD
Notes: An example of a volume study of the lateral ventricle looking at volume differences between patients with Alzheimer’s Disease and Controls (volume of ventricle was similar between those with AD and those who ultimately converted to AD; the questionables showed signs of AD but never converted). A volume study is in mm^3 and is looking at how many voxels are in an ROI.

## Slide 23: ROI Mean “Intensity” Analysis
Average vertex/voxel values or “point measures” over ROI
  MR Intensity (T1)
  Thickness, Sulcal Depth
Multimodal
  fMRI intensity
  FA values (diffusion data)
Notes: Vertex value will have intensity info from T1, Thickness, sulcal depth, etc. Since the way we derive ROIs is not by a map only (it is highly individualized to each subject’s anatomy) this allows you to take the mean vertex info from a region and get an accurate measure you can compare across subjects. i.e. average intensity over hippocampus

## Slide 24: ROI Mean “Intensity” Studies
Salat, et al, 2004.
Sigalovsky, et al, 2006
Greve, et al, 2008.
Physiological Noise
R1 Intensity
Thickness
fMRI
Notes: Left: R1 intensity value comparisons across gray matter regions (R1 is inverse of T1); Top right: Thickness of specific regions compared between young participants and old participants. Bottom right: Comparisons of physiological noise in fmri studies by point measure.

## Slide 25: Volume and Surface Atlases

## Slide 26: Volumetric Segmentation (aseg)
Caudate
Pallidum
Putamen
Amygdala
Hippocampus
Lateral Ventricle
Thalamus
White Matter
Cortex
Not Shown:
Nucleus Accumbens
Cerebellum
Whole Brain Segmentation: Automated Labeling of Neuroanatomical Structures in the Human Brain, Fischl, B., D.H. Salat, E. Busa, M. Albert, M. Dieterich, C. Haselgrove, A. van der Kouwe, R. Killiany, D. Kennedy, S. Klaveness, A. Montillo, N. Makris, B. Rosen, and A.M. Dale, (2002). Neuron, 33:341-355.
Notes: <number>
<footer>
<header>
<date/time>
-notice reference at bottom of slide

## Slide 27: Volumetric Segmentation Atlas Description
39 Subjects
14 Male, 25 Female
Ages 18-87
  Young (18-22): 10
  Mid (40-60): 10
  Old Healthy (69+): 8
  Old Alzheimer's (68+): 11
Siemens 1.5T Vision (Wash U)
Whole Brain Segmentation: Automated Labeling of Neuroanatomical Structures in the Human Brain, Fischl, B., D.H. Salat, E. Busa, M. Albert, M. Dieterich, C. Haselgrove, A. van der Kouwe, R. Killiany, D. Kennedy, S. Klaveness, A. Montillo, N. Makris, B. Rosen, and A.M. Dale, (2002). Neuron, 33:341-355.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 28: Automatic Surface Parcellation: Desikan/Killiany Atlas
Precentral Gyrus
Postcentral Gyrus
Superior Temporal Gyrus
An automated labeling system for subdividing the human cerebral cortex on MRI scans into gyral based regions of interest, Desikan, R.S., F. Segonne, B. Fischl, B.T. Quinn, B.C. Dickerson, D. Blacker, R.L. Buckner, A.M. Dale, R.P. Maguire, B.T. Hyman, M.S. Albert, and R.J. Killiany, (2006). NeuroImage 31(3):968-80.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 29: Desikan/Killiany Atlas
40 Subjects
14 Male, 26 Female
Ages 18-87
30 Nondemented
10 Demented
Siemens 1.5T Vision (Wash U)
An automated labeling system for subdividing the human cerebral cortex on MRI scans into gyral based regions of interest, Desikan, R.S., F. Segonne, B. Fischl, B.T. Quinn, B.C. Dickerson, D. Blacker, R.L. Buckner, A.M. Dale, R.P. Maguire, B.T. Hyman, M.S. Albert, and R.J. Killiany, (2006). NeuroImage 31(3):968-80.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 30: Automatic Surface Parcellation: Destrieux Atlas
Automatically Parcellating the Human Cerebral Cortex, Fischl, B., A. van der Kouwe, C. Destrieux, E. Halgren, F. Segonne, D. Salat, E. Busa, L. Seidman, J. Goldstein, D. Kennedy, V. Caviness, N. Makris, B. Rosen, and A.M. Dale, (2004). Cerebral Cortex, 14:11-22.
Notes: <number>
<footer>
<header>
<date/time>
Some subjects don’t have all these areas; reliability goes down

## Slide 31: Automatic Surface Parcellation: Destrieux Atlas
Automatically Parcellating the Human Cerebral Cortex, Fischl, B., A. van der Kouwe, C. Destrieux, E. Halgren, F. Segonne, D. Salat, E. Busa, L. Seidman, J. Goldstein, D. Kennedy, V. Caviness, N. Makris, B. Rosen, and A.M. Dale, (2004). Cerebral Cortex, 14:11-22.
58 Parcellation Units
12 Subjects
Notes: <number>
<footer>
<header>
<date/time>

## Slide 32: ROI Atlas Creation
Hand label N data sets
  Volumetric: CMA
  Surface Based:
    Desikan/Killiany
    Destrieux
Map labels to common coordinate system
Probabilistic Atlas
  Probability of a label at a vertex/voxel
    Maximum Likelihood (ML) Atlas Labels
  Curvature/Intensity means and stddevs
  Neighborhood relationships
Notes: How did we come up with these atlases that have the ROIs? CMA = Center for Morphemetric Analysis. We are creating a probabilistic Atlas based on this information. It includes curvature, intensity and neighborhood relationships info in it.

## Slide 33: Automatic Labeling
Transform ML labels to individual subject*
Adjust boundaries based on
  Curvature/Intensity statistics
  Neighborhood relationships
Result: labels are customized to each individual.
You can create your own atlases**
* Formally, we compute maximum a posteriori estimate of the labels given the input data
** Time consuming; first check if necessary
Notes: from atlas get prior information that help us decide how to do our images and from there fine tune

## Slide 34: Validation -- Jackknife
Hand label N Data Sets
Create atlas from (N-1) Data Sets
Automatically label the left out Data Set
Compare to Hand-Labeled
Repeat, Leaving out a different data set each time
Compute Dice coefficent for each N to check overlap of automatic & hand-labeled
Notes: compute a dice coefficient for each N to see how much the automatic labeled and hand labeled overlap

## Slide 35: Summary
Atlases: Probabilistic
ROIs are Individualized
Volume and Surface ROIs come in many different types
Measures for Studies
  Volume, Area
  Intensity, Thickness, Curvature
Multimodal Applications

## Slide 36: Tutorial
Simultaneously load:
  aparc+aseg.mgz (tkmedit)
  aparc.annot (tksurfer)
  FreeSurferColorLUT.txt
View Individual Stats Files
Group Table
  Create
  Load into spreadsheet

## Slide 38: Derived ROIs
Combined Volume-Surface segmentation
  aparc+aseg.mgz, a2005.aparc+aseg.mgz
White Matter Parcellation
  wmparc.mgz
Notes: Derived as in we combine different ROIs (aseg + aparc) or like wmparc where it’s just based on closest gray matter voxel

## Slide 39: Combined Segmentation
aparc+aseg
aseg
aparc
Use ROI volume as computed from aparc (more accurate)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 40: Gyral White Matter Segmentation
Nearest Cortical Label
to point in White Matter
aparc+aseg
wmparc
+
+
Notes: <number>
<footer>
<header>
<date/time>

## Slide 41
Segmentation: MRF
Preliminary Segmentation

## Slide 42
Segmentation: MRF
Final Segmentation