## Slide 1: FreeSurfer: Troubleshooting surfer.nmr.mgh.harvard.edu
Notes: <number>

## Slide 2: Quality Check Your Recon
Do your surfaces follow gm/wm borders?
Does the subcortical segmentation follow intensity boundaries?
Notes: <number>
-accurately follow boundaries?

## Slide 3
Output of Cortical Surface Reconstruction
Notes: <number>
-turn surfaces on/off to check; change brightness & contrast; is this where I would draw boundary?
-certain areas that don’t matter: surfaces near subcortical structures
-surfaces for wm/gm don’t check aseg for gm/wm

## Slide 4: Typical Errors
Pial Surface misplacement
Skull Strip Errors
WM Segmentation Errors
Intensity Normalization Errors
Topological Defect
Notes: <number>
-depends on quality of data
-won’t always see all these errors, tutorial overemphasizes them for you

## Slide 5
Dura or Blood Vessel
White/Gray OK, but
Pial Inaccurate
Pial Surface Misplacement
Dura and GM have extremely similar intensity characteristics on most T1-weighted sequences (but different T2*!). Typical fix: edit the brainmask.mgz to erase dura/blood vessels, and run:
recon-all -s <subject> -autorecon-pial
Notes: <number>
-dura corrupts AD studies b/c dura right next to ec and cannot tell what is gm and what is dura. know there is dura but can’t tell how much.
-only erase dura when see separation – a dark space between gm and dura.

## Slide 6: New Morphometry Protocol: Identifying Dura with Multi-echo MP-RAGE
*joint work with Andre van der Kouwe
Notes: <number>

## Slide 7
Skull Strip Error
brainmask.mgz
orig.mgz
Use “clone” tool to manually correct, or adjust watershed parameters and run (default wsthresh is 25, higher means strip less):
recon-all -skullstrip -wsthresh 35 -clean-bm -no-wsgcaatlas -s <subj>
recon-all -autorecon2 -autorecon3 -s <subj>
Notes: <number>

## Slide 8
Troubleshooting: Skull Strip
brainmask.mgz
orig.mgz
Or try gcut (be sure to check didn’t take too much!!):
recon-all -skullstrip -clean-bm -gcut -s <subj>
recon-all -autorecon2 -autorecon3 -s <subj>
Notes: <number>
careful to inspect edges of gm and cerebellum for over-aggressive cutting

## Slide 9
“Hypo-Intensities”
White Matter Lesions
Misclassified as gray matter
WM Segmentation Error
Fill in wm.mgz then run:
recon-all -s <subject> -autorecon2-wm -autorecon3
Notes: <number>
-if added control points, stuff surrounding it will get way too bright so want to fix by adding in wm in wm.mgz

## Slide 10
Eye Socket classified as WM due to Skull Strip Failure.
Erase in wm.mgz then run:
recon-all -s <subject> -autorecon2-wm -autorecon3
WM Segmentation Error
Notes: <number>
-fat shift of eyeball into brain

## Slide 11
Intensity Normalization Failure. Most WM in T1 volume (T1.mgz) should be close to 110. Can fix by adding “Control Points” to interior of wm. Beware partial voluming!
recon-all -s <subject> -autorecon2 -autorecon3
Intensity Normalization Error
Notes: <number>
-control points need to be placed on unpartialed voxels.
-correct pial surface by correcting wm surface
-add control points at base of strand
-don’t want to add far from base b/c hard to find voxel that isn’t gm

## Slide 12: Topology Fixer Error
Fornix
Pallidum and Putamen
hippocampus
Ventricles and Caudate
Cortical Defects
Holes
Handles
Automatically Fixed
Notes: <number>
-occipital horn at base, calcarine sulcus?
-explain hole and handle / cutting and filling
-topologically can’t tell difference b/c both could be handles or holes so that’s where error may happen

## Slide 13
White Matter
“disconnects”
orig.nofix will be
accurate
Topology Fixer Error
Add in wm.mgz then run:
recon-all -s <subject> -autorecon2-wm -autorecon3
Notes: <number>
fill in gap manually
(add in snapshot of matching slice in brainmask to show how difficult it is to diagnose)
-If the ?h.orig surface misses white matter that is accurately labeled in the wm.mgz or extends into regions where there is no wm in the wm.mgz, then there is an incorrectly fixed topological defect.

## Slide 14: What are the Common Interventions?
Manually edit the wm.mgz to change incorrectly labeled voxels (only for small errors).
Manually edit the brainmask.mgz to erase dura/vasculature.
Adjust watershed parameters to fix large-scale skull-strip errors or use –gcut to fix large-scale skull-strip errors.
Manually erase regions of left in skull on a few slices
Control Points – add locations that are in the interior of the white matter and <110 to bring regional wm intensity up.
Notes: <number>
-don’t spend a lot of time on talairach b/c use it very little but make sure it’s pretty accurate

## Slide 15: How Know What to Edit?
If pial surface includes too much:
  edit brainmask.mgz
If it affects the white surface (too much/little):
  edit the wm.mgz (if segmentation error)
  add control points (if normalization error)

## Slide 16: Troubleshooting – Advice
CONTEXT
AMBIGUITY
CONSISTENCY
SPEED
Notes: <number>
we as humans are really bad at reconstructing 3D images so if doing lots of editing may be making it worse.
If doing lots of editing, may want to start over and take a minimalist approach
if try to make every voxel as accurate as you can, will dramatically reduce reliability while only moderately increasing accuracy

## Slide 17: Troubleshooting – Advice
CONTEXT
Always look at the data in multiple views and scroll back and forth a few slices – 3D structure is difficult to discern!
AMBIGUITY
CONSISTENCY
SPEED
Notes: <number>
we as humans are really bad at reconstructing 3D images so if doing lots of editing may be making it worse.

## Slide 18: Troubleshooting – Advice
CONTEXT
Always look at the data in multiple views and scroll back and forth a few slices – 3D structure is difficult to discern!
AMBIGUITY
Don’t edit too much! This will reduce reliability and is almost never needed. If unsure, leave it.
Even one or two missing voxels can cause large-scale defects, so very minor editing (e.g. filling in white matter voxels that are holes, or erasing handles) may fix the problem.
CONSISTENCY
SPEED
Notes: <number>
we as humans are really bad at reconstructing 3D images so if doing lots of editing may be making it worse.
If doing lots of editing, may want to start over and take a minimalist approach
if try to make every voxel as accurate as you can, will dramatically reduce reliability while only moderately increasing accuracy

## Slide 19: Troubleshooting – Advice
CONTEXT
Always look at the data in multiple views and scroll back and forth a few slices – 3D structure is difficult to discern!
AMBIGUITY
Don’t edit too much! This will reduce reliability and is almost never needed. If unsure, leave it.
Even one or two missing voxels can cause large-scale defects, so very minor editing (e.g. filling in white matter voxels that are holes, or erasing handles) may fix the problem.
CONSISTENCY
Edit consistently within and across subjects.
SPEED
Notes: <number>

## Slide 20: Troubleshooting – Advice
CONTEXT
Always look at the data in multiple views and scroll back and forth a few slices – 3D structure is difficult to discern!
AMBIGUITY
Don’t edit too much! This will reduce reliability and is almost never needed. If unsure, leave it.
Even one or two missing voxels can cause large-scale defects, so very minor editing (e.g. filling in white matter voxels that are holes, or erasing handles) may fix the problem.
CONSISTENCY
Edit consistently within and across subjects.
SPEED
You will get faster with time; certain sections go faster.
Notes: <number>

## Slide 21: Must rerun to fix errors
recon-all -autorecon2 -autorecon3 (Stages 6+)
Skull strip error (after fixed watershed/cloned)
recon-all -autorecon2 -autorecon3 (Stages 10+)
Added control points
recon-all -autorecon2-wm -autorecon3 (Stages 13+)
Edited wm.mgz
recon-all -autorecon-pial (Stage 19+)
Edited brainmask.mgz
Notes: <number>

## Slide 22: Processing Stream Order
http://surfer.nmr.mgh.harvard.edu/fswiki/ReconAllDevTable
Notes: <number>

## Slide 23: Or Make Life Easier
recon-all -make all -s subjid

## Slide 24: Start Over
recon-all -all -clean -s subjid

## Slide 25: Tutorial Tips
DO NOT open tkmedit & tksurfer from the same terminal window. (Use two terminal windows)
You CANNOT type commands in a terminal window if you are running tkmedit or tksurfer from it. (Open a new terminal window to do this.)

## Slide 26: See Edits Made
recon-all –show-edits -s subjid