## Slide 1: Surface-based Group Analysis in FreeSurfer

## Slide 2
Outline
GLM Theory
FSGD File
Processing Stages
Vertex-wise Analysis
Correction for multiple comparisons
Interactive/Automated GUI (QDEC)

## Slide 3
Surface-based Study (Thickness)

## Slide 4: Surface-based Measures
Morphometric (eg, thickness)
Functional
PET
MEG/EEG
Diffusion (?) sampled just under the surface

## Slide 5: Intersubject Registration

## Slide 6
Coordinate Systems: 3D (Volumetric)
3D Coordinate System
  XYZ
  RAS (Right-Anterior-Superior)
  CRS (Column-Row-Slice)
  Origin (XYZ=0, eg, AC)
  MR Intensity at each XYZ
x
z
y

## Slide 7: Coordinate Systems: 2D (Surface)
superior temporal
calcarine
central
sylvian
anterior
posterior
pial
inflated
Curvature
SULCUS (+)
GYRUS (-)
Sheet: 2D Coordinate System (X,Y)
Sphere: 2D Coordinate System
Latitude and Longitude 
Continuous, no cuts
Value at each point (eg, thickness)
x
y



## Slide 8
Volumetric Intersubject Registration
Affine/Linear
  Translate
  Rotate
  Stretch
  Shear
  (12 DOF)
Match Intensity, Voxel-by-Voxel
Problems
Can use nonlinear volumetric (cf CVS)

## Slide 9: Surface-based Intersubject Registration
Subject 2
Subject 1
Translate, Rotate, Stretch, Shear (12 DOF)
Match Curvature, Vertex-by-Vertex
Nonlinear Stretching (“Morphing”) allowed (area regularization)
Actually done on sphere
“Spherical Morph”
Curvature “Intensity”
SULCUS (+)
GYRUS (-)
Codes folding pattern

## Slide 10: Surface-based Intersubject Registration
  Gray Matter-to-Gray Matter (it’s all gray matter!)
  Gyrus-to-Gyrus and Sulcus-to-Sulcus
  Some minor folding patterns won’t line up
  Fully automated, no landmarking needed
  Atlas registration is probabilistic, most variable regions get less weight.
  Done automatically in recon-all

## Slide 11: GLM Theory: Design Matrix
y11
y12
y13
y21
y22
y23
G1 G2 G1*Age G2*Age
1 0 20 0
1 0 25 0
1 0 30 0
0 1 0 18
0 1 0 23
0 1 0 35
b1
b2
m1
m2
=
.
Data Design Matrix Regression Coefficients
y = X*

## Slide 12: GLM Theory: Contrasts
y11
y12
y13
y21
y22
y23
G1 G2 G1*Age G2*Age
1 0 20 0
1 0 25 0
1 0 30 0
0 1 0 18
0 1 0 23
0 1 0 35
b1
b2
m1
m2
=
.
CGroup = [1 -1 0 0] Group diff=0?
CAge = [0 0 0.5 0.5] Mean slope=0?
CGroupXAge = [0 0 +1 -1] Group/Age InterX?

## Slide 13: Vertex-wise Analysis and Inference
y = X*
XtX)-1Xty
=C*
p-value/significance
value between 0 and 1
closer to 0 means more significant
FreeSurfer stores p-values as –log10(p):
0.1=10-1sig=1, 0.01=10-2sig=2
sig.mgh files
Signed by sign of 
p-value is for an unsigned test

## Slide 14
Need:
X (Design Matrix)
C (Contrast Matrix or Matrices)
y (Data)

## Slide 15
Specifying X and C
Manually create X – text editor
  Manually create C
FSGD file – text editor
  FreeSurfer creates X
  Manually create C
QDEC – spread sheet, etc
  FreeSurfer creates X and C

## Slide 16: FreeSurfer Group Descriptor (FSGD) File
Simple text file (ascii, clear text)
List of all subjects in the study
Accompanying demographics

## Slide 17: FSGD Format
GroupDescriptorFile 1
Class Male
Class Female
Variables Age Weight IQ
Input bert Male 10 100 1000
Input fred Male 15 150 1500
Input jenny Female 20 200 2000
Input margaret Female 25 250 2500
One Discrete Factor (Gender) with Two Levels (M&F)
Three Continuous Variables: Age, Weight, IQ
$SUBJECTS_DIR/bert

## Slide 18: FSGD  X (Automatic)
DODS – Different Offset, Different Slope
C = [-1 1 0 0 0 0 0 0]
}
Tests for the difference in intercept/offset between groups
1 0 10 0 100 0 1000 0
1 0 15 0 150 0 1500 0
0 1 0 20 0 200 0 2000
0 1 0 25 0 250 0 2500
X =
Male Group
Female Group
Female*Age
Male*Age
Weight
Age
IQ
C = [ 0 0 -1 1 0 0 0 0]
}
Tests for the difference in age slope between groups
{
Manual

## Slide 19: FSGD Terminology
Continuous Variables/Factors: Age, IQ, Volume, etc
Discrete Variables/Factors: Gender, Handedness, Diagnosis
Levels of Discrete :
Handedness: Left and Right
Gender: Male and Female
Diagnosis: Normal, MCI, AD
Cannot specify Discrete Factors in FSGD
Group or Class: Specification of All Discrete Factors:
Left-handed Male MCI
Right-handed Female Normal

## Slide 20: Number of Regressors
Each Group/Class:
  Has its own Intercept
  Has its own Slope (for each continuous variable)
NRegressors = NClasses*(NVariables+1)

## Slide 21: Data (y): Thickness Study
$SUBJECTS_DIR/bert/surf/lh.thickness
$SUBJECTS_DIR/fred/surf/lh.thickness
$SUBJECTS_DIR/jenny/surf/lh.thickness
$SUBJECTS_DIR/margaret/surf/lh.thickness
…

## Slide 22: Assemble Data: mris_preproc
--fsgd FSGDFile : Specify subjects thru FSGD File
--hemi lh : Process left hemisphere
--meas thickness : $SUBJECTS_DIR/subjectid/surf/hemi.thickness
--target fsaverage : common space is subject fsaverage
--o lh.thickness.mgh : output “volume-encoded surface file”
Lots of other options!
mris_preproc --help
lh.thickness.mgh – file with thickness maps for all subjects  Input to Smoother or GLM
See also: recon-all -qcache

## Slide 23: Spatial Smoothing
Why should you smooth?
Might Improve CNR
Improve intersubject registration (functional)
How much smoothing?
Blob-size
Typically 10-20 mm FWHM
Surface smoothing more forgiving than volume-based

## Slide 24: Volume-based Smoothing
  Smoothing is averaging of nearby voxels
7mm FWHM
14mm FWHM

## Slide 25: Volume-based Smoothing
  5 mm apart in 3D
  25 mm apart on surface!
  Kernel much larger
  Averaging with other tissue types (WM, CSF)
  Averaging with other functional areas
14mm FWHM

## Slide 26: Surface-based Smoothing
superior temporal
calcarine
central
sylvian
anterior
posterior
Sheet: 2D Coordinate System (X,Y)
Sphere: 2D Coordinate System ()
  Smoothing is averaging of nearby vertices

## Slide 27: Surface Smoothing
mri_surf2surf --help
Loads lh.thickness.mgh
2D surface-based smoothing
Specify FWHM (eg, fwhm = 10 mm)
Saves lh.thickness.sm10.mgh
Can be slow (~10-60min)
recon-all -qcache

## Slide 28: Estimation and Inference: mri_glmfit
Reads in FSGD File and constructs X
Reads in your contrasts (C1, C2, etc)
Loads data (y=lh.thickness.sm10.mgh)
Fits GLM (ie, computes )
Computes contrasts (=C*)
t or F ratios, significances
Significance -log10(p) (.01  2, .001  3)

## Slide 29: mri_glmfit
mri_glmfit
--y lh.thickness.sm10.mgh
--fsgd gender_age.txt
--C age.mat –C gender.mat
--surf fsaverage lh
--cortex
--glmdir lh.gender_age.glmdir
Creates: lh.gender_age.glmdir/
beta.mgh – parameter estimates
rvar.mgh – residual error variance
etc …
age/
sig.mgh – -log10(p), uncorrected
gamma.mgh, F.mgh
gender/
sig.mgh – -log10(p)
gamma.mgh, F.mgh
mri_glmfit --help

## Slide 30
Visualization with tksurfer
View->Configure->Overlay
Threshold:
-log10(p),
Eg, 2=.01
Saturation:
-log10(p),
Eg, 5=.00001
False
Dicovery
Rate
Eg, .01
File->LoadOverlay

## Slide 31
Visualization with tksurfer
File->
Load Group Descriptor File …

## Slide 32: Problem of Multiple Comparisons
p < 0.10
p < 0.01
p < 10-7

## Slide 33: Correction for Multiple Comparisons
Cluster-based
  Monte Carlo simulation
  Permutation Tests
  Surface Gaussian Random Fields (GRF)
    There but not fully tested
False Discovery Rate (FDR) – built into tksurfer and QDEC. (Genovese, et al, NI 2002)

## Slide 34: Clustering
Choose a vertex-wise threshold
  Eg, 2 (p<.01), or 3 (p<.001)
  Sign (pos, neg, abs)
A cluster is a group of connected (neighboring) vertices above threshold
Cluster has a size (area in mm2)
p<.01 (-log10(p)=2)
Negative
p<.0001 (-log10(p)=4)
Negative

## Slide 35: Cluster-based Correction for Multiple Comparisons
Simulate data under Null Hypothesis:
  Synthesize Gaussian noise and then smooth (Monte Carlo)
  Permute rows of design matrix (Permutation, orthog)
Analyze, threshold, cluster, max cluster size
Repeat 10,000 times
Analyze real data, get cluster sizes
P(cluster) = #MaxClusterSize > ClusterSize/10000
mri_glmfit-sim

## Slide 36
Command-line Processing Stages
Model (X, FSGD) and Contrasts (C)
Assemble Data (mris_preproc)
  Resample into Common Space
  Concatenate into one file
Smooth (mri_surf2surf)
Fit Model (Estimate) (mri_glmfit)
Correct for multiple comparisons (mri_glmfit-sim)
Visualize (tksurfer)
recon-all -qcache

## Slide 37
QDEC – An Interactive Statistical Engine GUI
Query – Select subjects based on Match Criteria
Design – Specify discrete and continuous factors
Estimate – Fit Model
Contrast – Automatically Generate Contrast Matrices
Interactive – Makes easy things easy (that used to be hard)
…a work in progress
No Query yet
Two Discrete Factors (Two Levels)
Two Continuous Factors
Surface only

## Slide 38
QDEC – Spreadsheet
fsid gender age diagnosis Left-Cerebral-White-Matter-Vol
011121_vc8048 Female 70 Demented 202291
021121_62313-2 Female 71 Demented 210188
010607_vc7017 Female 73 Nondemented 170653
021121_vc10557 Male 75 Demented 142029
020718_62545 Male 76 Demented 186087
020322_vc8817 Male 77 Nondemented 149810
qdec.table.dat – spreadsheet with subject information – spreadsheet can be huge!
Female
Male
gender.levels
Demented
Nondemented
diagnosis.levels
Discrete Factors need a
factorname.level file

## Slide 39: Tutorial
Command-line Stream
  Create an FSGD File for a thickness study
  Age and Gender
  Run
    mris_preproc
    mri_surf2surf
    mri_glmfit
    mri_glmfit-sim
    tksurfer
QDEC – same data set

## Slide 41: Another FSGD Example
GroupDescriptorFile 1
Class MaleRight
Class MaleLeft
Class FemaleRight
Class FemaleLeft
Variables Age
Input bert MaleLeft 10
Input fred MaleRight 15
Input jenny FemaleRight 20
Input margaret FemaleLeft 25
Class = Group
Two Discrete Factors
  Gender: Two Levels (M&F)
  Handedness: Two Levels (L&R)
One Continuous Variable: Age

## Slide 42: Interaction Contrast
GroupDescriptorFile 1
Class MaleRight
Class MaleLeft
Class FemaleRight
Class FemaleLeft
Input bert MaleLeft
Input fred MaleRight
Input jenny FemaleRight
Input margaret FemaleLeft
Two Discrete Factors (no continuous, for now)
  Gender: Two Levels (M&F)
  Handedness: Two Levels (L&R)
Four Regressors (Offsets)
  MR (1), ML (2), FR (3), FL (4)
M
F
R
L
1
4
3
2



3-1)- 4-2)
1+2+ 3-4
C = [-1 +1 +1 -1]


## Slide 43: FSGDF X
1 0 10 100 1000
1 0 15 150 1500
0 1 20 200 2000
0 1 25 250 2500
DOSS – Different Offset, Same Slope
X =
C = [-1 1 0 0 0]
#Regressors = Nv+Nc = 3+2=5  Fewer regressors than DODS
DOF = #Rows - #Regressors
Male Class
Female Class
Age for Males and Females
 Same test, different vector
Input:
y
X
C
Notes: .