## Slide 1: FreeSurfer: Troubleshooting surfer.nmr.mgh.harvard.edu

## Slide 2: Quality Check Your Recon
Do your surfaces follow gm/wm borders?
Does the subcortical segmentation follow intensity boundaries?
Notes: -accurately follow boundaries?

## Slide 3
Output of Cortical Surface Reconstruction
Notes: -turn surfaces on/off to check; change brightness & contrast; is this where I would draw boundary?
-certain areas that don’t matter: surfaces near subcortical structures
-surfaces for wm/gm don’t check aseg for gm/wm

## Slide 4: Typical Errors
Pial Surface misplacement
Skull Strip Errors
WM Segmentation Errors
Intensity Normalization Errors
Topological Defect
Notes: -depends on quality of data
-won’t always see all these errors, tutorial overemphasizes them for you

## Slide 5
Dura or Blood Vessel
White/Gray OK, but
Pial Inaccurate
Pial Surface Misplacement
Dura and GM have extremely similar intensity characteristics on most T1-weighted sequences (but different T2*!). Typical fix: edit the brainmask.mgz to erase dura/blood vessels, and run:
recon-all -s <subject> -autorecon2-pial -autorecon3
Notes: dura corrupts AD studies b/c dura right next to ec and cannot tell what is gm and what is dura. know there is dura but can’t tell how much. only erase dura when see separation – a dark space between gm and dura.

## Slide 6
Skull Strip Error
brainmask.mgz
orig.mgz
Use “clone” tool to manually correct, or adjust watershed parameters and run (default wsthresh is 25, higher means strip less):
recon-all -skullstrip -wsthresh 35 -clean-bm -no-wsgcaatlas -s <subj>
recon-all -s <subject> -autorecon2 -autorecon3

## Slide 7
Troubleshooting: Skull Strip
brainmask.mgz
orig.mgz
Or try gcut (be sure to check didn’t take too much!!):
recon-all -skullstrip -clean-bm -gcut -s <subj>
recon-all -autorecon2 -autorecon3 -s <subj>
Notes: careful to inspect edges of gm and cerebellum for over-aggressive cutting

## Slide 8
“Hypo-Intensities”
White Matter Lesions
Misclassified as gray matter
WM Segmentation Error
Fill in wm.mgz then run:
recon-all -s <subject> -autorecon2-wm -autorecon3
Notes: -if added control points, stuff surrounding it will get way too bright so want to fix by adding in wm in wm.mgz

## Slide 9
Eye Socket classified as WM due to Skull Strip Failure.
Erase in wm.mgz then run:
recon-all -s <subject> -autorecon2-wm -autorecon3
WM Segmentation Error
Notes: -fat shift of eyeball into brain

## Slide 10
Intensity Normalization Failure. Most WM in T1 volume (T1.mgz) should be close to 110. Can fix by adding “Control Points” to interior of wm. Beware partial voluming!
recon-all -s <subject> -autorecon2 -autorecon3
Intensity Normalization Error
Notes: -control points need to be unpartialed voxels.
-correct pial surface by correcting wm surface
-add control points at base of strand
-don’t want to add far from base b/c hard to find voxel that isn’t gm

## Slide 11: Topology Fixer Error
Fornix
Pallidum and Putamen
hippocampus
Ventricles and Caudate
Cortical Defects
Holes
Handles
Automatically Fixed
Notes: -occipital horn at base, calcarine sulcus?
-explain hole and handle / cutting and filling
-topologically can’t tell difference b/c both could be handles or holes so that’s where error may happen

## Slide 12
White Matter
“disconnects”
orig.nofix will be
accurate
Topology Fixer Error
Add in wm.mgz then run:
recon-all -s <subject> -autorecon2-wm -autorecon3
Notes: fill in gap manually
(add in snapshot of matching slice in brainmask to show how difficult it is to diagnose)
-If the ?h.orig surface misses white matter that is accurately labeled in the wm.mgz or extends into regions where there is no wm in the wm.mgz, then there is an incorrectly fixed topological defect.

## Slide 13: How Know What to Edit?
If it affects the pial surface:
  edit brainmask.mgz
If it affects the white surface:
  edit the wm.mgz (if segmentation error)
  add control points (if normalization error)
(≈98% of surface accurate in about 98% of cases for good data)

## Slide 14: Must rerun to fix errors
recon-all -autorecon2 -autorecon3 (Stages 6+)
Skull strip error (after fixed watershed/cloned)
recon-all -autorecon2-cp -autorecon3 (Stages 10+)
Added control points
recon-all -autorecon2-wm -autorecon3 (Stages 13+)
Edited wm.mgz
recon-all -autorecon2-pial -autorecon3 (Stage 19+)
Edited brainmask.mgz

## Slide 15: Troubleshooting – Advice
CONTEXT
Always look at the data in multiple views and scroll back and forth a few slices – 3D structure is difficult to discern!
AMBIGUITY
Don’t edit too much! This will reduce reliability and is almost never needed. If unsure, leave it.
Even one or two missing voxels can cause large-scale defects, so very minor editing (e.g. filling in white matter voxels that are holes, or erasing handles) may fix the problem.
CONSISTENCY
Edit consistently within and across subjects.
SPEED
You will get faster with time; certain sections go faster.